## Slide 1: HYDROLOGY
Precipitation part 1
Yasir Alrubaye

## Slide 2: Formation of type of precipitation
Types of precipitation
Cyclonic precipitation
Convective precipitation
Orographic precipitation

## Slide 3: Cyclonic precipitation

## Slide 4: Convective precipitation

## Slide 5: Orographic precipitation

## Slide 6: Measurement of precipitation
Rain Gages
The standard 8" gage
Tipping-bucket Rain gages
The weighing-type gage

## Slide 7: The standard 8" gage
Rain pass from the collector into a cylindrical measuring tube inside the overflow can. The measuring tube has a cross-sectional area one-tenth that collector that of collector so that 0.1-in rainfall will fill the tube to a depth of 1-in.
To find the diameter of measuring tube this form can be used.

## Slide 8: Tipping-bucket Rain gages
In the tipping-bucket gage water caught in the collector and guided into a two-compartment bucket 0.1 mm or some other designed quantity of rain will fill one compartment (partition) and overbalance the bucket so that it tips, emptying into a reservoir and moving the second compartment into place below the funnel. As bucket is tipped, it actuates an electric circuit.

## Slide 9: The weighing-type gage
The weighing-type gage is weighs the rain which falls into a bucket set on the platform of spring or level balance. The increasing weight of bucket and its content is recording on a chart. The record thus shows the accumulation of precipitation.

## Slide 10: Estimating the missing precipitation data.
Simple arithmetic: -
In this method the amounts at the index station are equal weighted with all other stations. This method used when the normal annual precipitation at any index station differs from that at the station in question by less than 10 percent.
Normal-ratio method: -
In this method the amounts at the index station are weighted by the ratio of the normal-annual-precipitation values. This method used when the normal annual precipitation at any index station differs from that at the station in question by more than 10 percent.
X
A
B
C

## Slide 11: Example: Find precipitation of station d using data in Table (3-1).
Station name | Precipitation (cm) | Annual precipitation (cm)
A | 4.2 | 44.1
B | 3.5 | 36.8
C | 4.8 | 47.2
D | ? | 38.5
Solution:
Average method:
Normal-ratio method: