## Slide 1: HYDROLOGY
Ground Water and wells part 1
Yasir Alrubaye

## Slide 2: Groundwater and Wells
Groundwater is an important phase of the hydrologic cycle. Most of the flow returning streams creates from subsurface water, while a large part of flow of transient streams may percolate beneath the surface

## Slide 3: Definitions
Aquifers: a geologic formation which contains water and transmits it from one point to another in quantities sufficient to permit economic development.
Movement of groundwater: is the water movement in the soil below capillary tables.
Transmissibility: representation of the flow rate per day through a section 1 ft or 1 m wide and the thickness of the aquifer under unit head (slope 1ft/1ft).
In 1856 Darcy confirmed the applicability of principles of fluid flow in capillary tubes, developed several years earlier by Hagen and Poiseuille, to the flow of water in permeable media. Darcy's law can be written as:
The discharge of the aquifer can be found by from:
Transmissibility: representation of the flow rate per day through a section 1 ft or 1 m wide and the thickness of the aquifer under unit head (slope 1ft/1ft).
The discharge can be found from transmissibility as:

## Slide 4: Unconfined aquifers
Unconfined aquifers: is the aquifer has a free water table and impervious bed. The groundwater has the ability of moving vertically and horizontally. The piezometric line is the water table.

## Slide 5: Confined aquifers
Confined aquifers: is the aquifer which has a pressurized flow in between two impervious layers. There is horizontal flow (one direction flow). The piezo metric-line is higher than the water table.

## Slide 6: Simi-confined aquifers
Simi-confined aquifers: is the aquifer that has an Aquitard Simi-previous layer with small hydraulic conductivity where the flow direction though it is vertically. The aquitard separate two layers where the layer below Aquitard named confined and the layer above Aquitard named unconfined.

## Slide 7: Flow in Aquifer with Well Systems
The flow toward the well in horizontal direction with hydrostatic pressure of cylinder surface at radius (r). The head of the hydrostatic pressure can be find from the equation:

## Slide 8: Well with confined aquifer
Using integration the distribution head through the aquifer can be find from:
Where:
the hydrostatic head of water at r distance from the well,
the hydrostatic head of water at R distance,
the radius from the well until reach the hydrostatic head equal to the main head before the well,
well radius, and
the radius from well to any point.

## Slide 9: Discharge of the aquifer can be found from:
Sub equation 2, 3, and 4 in equation 1