## Slide 1: SURVEYING CHAPTER- 2 / DISTANCE MEASUREMENT
Asst. Lect. Ali Khalid
Al-Mansour University College
Civil Engineering Department
Second Year/ 2015-2016

## Slide 2: Distance Measurements
There are two main methods of determining the distances between points on a surface earth.
1. Direct Measurement
In this method, distances are actually measured on the surface using measurement instruments.
2. Computative Measurement
Calculations are made to measure distances as in tacheometry and triangulation (or chain) surveying.
Methods of measuring distances
1. Measuring Chain. 2. Measuring Wheel.
3. Measuring Tape.

## Slide 3
2. Measuring Wheel:
It is used for fast measurements and lower
accuracy surveys.
Although its accuracy reduced on a rough terrain,
it provides good accurate in measurements on a
smooth surface such as pavement.
1. Measuring Chain:
It is easy to read and designed
for a rough terrain.
Chains are heavy and, thus,
sag is a major error.
How does
It work?

## Slide 4
3. Measuring Tapes:
Depending on materials used, tapes are classified as:
Cloth or linen tapes: Such tape is light and flexible, hence it is easy to handle but:
It is easily affected by moisture and, thus, gets shrunk.
It extends due to stretching.
It is likely to twist and tangle.
a. Linen Tape

## Slide 5
b. Metallic tape: This tape is reinforced with copper wires to prevent stretching or twisting of fibers. It is used for measuring accurate distances.
c. Steel tape: It is used to measure short distances.
b. Metallic Tape c. Steel Tape
d. Invar tape: It is more expensive and used for high degree of precision in measurements.

## Slide 6
4. Measuring Laser:
Work can be done better, faster, and more precise using laser measurements.
It easily measures lines that are difficult of access such as across lakes and rivers, etc.
Disadvantage of laser measurements is the cost of the equipment.
How does
It work?