## Slide 1: SURVEYING CHAPTER- 4 / LEVELS AND LEVELING
Asst. Lect. Ali Khalid
Al-Mansour University College
Civil Engineering Department
Second Year/ 2015-2016

## Slide 2: Levels and Leveling
Leveling is the most widely used method for obtaining the elevations of ground points relative to a reference datum.
Datum: is any reference surface to which the elevations of points are referred. The most commonly used datum is mean sea level (MSL).
Mean Sea Level (MSL): is the average height of the sea for all stages of the tides. At any particular place, MSL is established by finding the mean sea level (free of tides) after averaging tide heights over a long period of time.
Leveling involves the measurement of vertical distance relative to a horizontal line of sight. Hence it requires a graduated staff for the vertical measurements and an instrument that will provide a horizontal line of sight.

## Slide 3
Principles of Leveling
Level Line or Level Surface: is one which at all points is normal to the direction of the force of gravity as defined by a freely suspended plumb-bob.
Vertical Line: A vertical line at a point is the line connecting the point to the center of the earth. It is the plumb line at that point. Thus the difference in level between A and B is the distance A’B, provided that the non-
parallelism of level surfaces
is ignored.
Horizontal Line or Surface:
is one that is normal to the
direction of the force of
gravity at a particular point
shows a horizontal line through
point C.

## Slide 4
METHODS OF LEVELING
Hydrostatic Leveling:
It is suitable for measurements in buildings. The hydrostatic leveling works on the principle of communicating vessels: are associated with water-filled container at the lowest point through tubes to each other, it turns into an all containers of the same water level.
Direct Leveling:
In this method, horizontal sight is taken on a graduated staff and the difference in elevation between line of sight and ground at which staff is held can be calculated.
Indirect Leveling:
instruments such as theodolite and total station are used to measure the vertical angles. Then using trigonometric relations to calculate difference sin elevation, thus, it is called trigonometric leveling.

## Slide 5
TERMS USED IN DIRECT METHOD OF LEVELLING
Back Sight (BS): It is the sight taken on a level staff held on the point of known elevation. It is always the first reading after the instrument is set in a place.
Fore Sight (FS): This is the last reading taken from the instrument station before shifting it or just before ending the work.
Intermediate Sight (IS): it is any other staff reading taken from the setting of the level between the back sight and fore sight.
Benchmark: A fixed reference point or object, the elevation of which is known.
Station: the point whose elevation is to be found out. It is the place where the staff is held in position. The point at which the level is set up is not a station.

## Slide 6
Height of Instrument(H.I.): The height of the line of sight of the telescope above a station or control point (h.i). Sometimes referred to as the actual elevation of the telescope.
Turning Point (TP): This is a point on which both fore sights and back sights are taken. After taking fore sight on this point instrument is set at another point and back sight is taken on the staff held at the same point.

## Slide 7
Methods of Computation
1. Height of Instrument:
HI = Elev. of BM + BS reading
Elev. of station = HI – (FS or IS) reading
2. Rise and Fall:
If is (+) then called Rise (R)
If is (-) then called fall (F)

## Slide 8
Example (1)
For a given figure below, find the elevation of point B.
Sol:
Height of Instrument Method | Rise and Fall Method
H.I = elev. (A) + BS = 755.11+5.1 = 760.21 m Elev. (B) = H.I – FS = 760.21 – 1.23 = 758.98 m | = BS – FS = 5.1 – 1.23 = 3.87 m (R) Elev. (B) = Elev. (A) + R = 755.11 + 3.87= 758.98 m
Height of Instrument Method | Rise and Fall Method
H.I = elev. (A) + BS = 755.11+5.1 = 760.21 m Elev. (B) = H.I – FS = 760.21 – 1.23 = 758.98 m | 

## Slide 9
Example (2)
For the given figure below, if the elevation of BM-A is 2053.18 foot, find the elevation of BM using both height of instrument and rise and fall methods and check the results (All dimensions are in foot).

## Slide 10
Height of Instrument Method:
BS - FS = Last Elev. – First Elev. = -33.74 m
Rise and Fall Method:
BS - FS = - F = Last Elev. – First Elev. = -33.74 m
Station | BS | FS | HI | Elevation | Remarks
A | 1.33 |  | 2054.51 | 2053.18 | BM
B | 0.22 | 8.37 | 2046.36 | 2046.14 | TP1
C | 0.96 | 7.91 | 2039.41 | 2038.45 | TP2
D | 0.46 | 11.72 | 2028.15 | 2027.69 | TP3
E |  | 8.71 |  | 2019.44 | BM
Sum | 2.97 | 36.71 |  |  | 
Station | BS | FS | R | F | Elevation | Remarks
A | 1.33 |  |  | 7.04 | 2053.18 | BM
B | 0.22 | 8.37 |  | 7.69 | 2046.14 | TP1
C | 0.96 | 7.91 |  | 10.76 | 2038.45 | TP2
D | 0.46 | 11.72 |  | 8.25 | 2027.69 | TP3
 |  | 8.71 |  | 0 | 2019.44 | BM
Sum | 2.97 | 36.71 |  | 33.74 |  |