## Slide 1: SURVEYING CHAPTER- 4 / LEVELS AND LEVELING
Asst. Lect. Ali Khalid
Al-Mansour University College
Civil Engineering Department
Second Year/ 2015-2016

## Slide 2
Example (3)
In a construction of housing complex project, the following set of reading was obtained: 2.156, 1.945, 2.887, 1.985, 0.792, and 2.774. The first reading was taken on a bench mark of 50.733 m elevation and the instrument was shifted after each two readings, compute the elevation of last reading which is nearby the project and fixed as BM using both HI and R&F methods and check the results.
Solution: Draw the sketch as follows:

## Slide 3
Height of Instrument Method:
BS - FS = Last Elev. – First Elev. = - 0.869m
Rise and Fall Method:
BS - FS = - F = Last Elev. – First Elev. = - 0.869m
Station | BS | FS | HI | Elevation | Remarks
A | 2.156 |  | 52.889 | 50.733 | BM
B | 2.887 | 1.945 | 53.831 | 50.944 | TP1
C | 0.792 | 1.985 | 52.638 | 51.846 | TP2
D |  | 2.774 |  | 49.864 | BM
Sum | 5.835 | 6.704 |  |  | 
Station | BS | FS | R | F | Elevation | Remarks
A | 2.156 |  | 0.211 |  | 50.733 | BM
B | 2.887 | 1.945 | 0.902 |  | 50.944 | TP1
C | 0.792 | 1.985 |  | 1.982 | 51.846 | TP2
D |  | 2.774 |  |  | 49.864 | BM
Sum | 5.835 | 6.704 | 1.113 | 1.982 |  | 

## Slide 4
Example (4)
In a construction of railway, the following set of readings was obtained: 2.5, 1.0, 1.5, 1.8, 2.3, 2.9, 1.3, 3.2, 2.8, 2.0, and 1.5. The instrument was shifted after the fourth and seventh reading. The last reading was taken on a BM of elevation 253.40 m. Find the elevation of all stations by both height of instrument and rise & fall methods.
Solution: Draw a sketch:
BS - FS = Last Elev. – First Elev.
8.0 – 4.6 = 253.4 – 1st Elev.
1st Elev. = 250.0 m

## Slide 5
1. Height of Instrument Method:
Solution: Draw the figure as follows:
Station | BS | IS | FS | HI | Elevation | Remarks
1 | 2.5 |  |  | 252.5 | 250.0 | 
2 |  | 1.0 |  |  | 251.5 | 
3 |  | 1.5 |  |  | 251.0 | 
4 | 2.3 |  | 1.8 | 253.0 | 250.7 | T.P1
5 |  | 2.9 |  |  | 250.1 | 
6 | 3.2 |  | 1.3 | 254.9 | 251.7 | T.P2
7 |  | 2.8 |  |  | 252.1 | 
8 |  | 2.0 |  |  | 252.9 | 
9 |  |  | 1.5 |  | 253.4 | BM

## Slide 6
Station | BS | IS | FS | R | F | Elevation | Remarks
1 | 2.5 |  |  |  |  | 250.0 | 
2 |  | 1.0 |  | 1.5 |  | 251.5 | 
3 |  | 1.5 |  |  | 0.5 | 251.0 | 
4 | 2.3 |  | 1.8 |  | 0.3 | 250.7 | T.P1
5 |  | 2.9 |  |  | 0.6 | 250.1 | 
6 | 3.2 |  | 1.3 | 1.6 |  | 251.7 | T.P2
7 |  | 2.8 |  | 0.4 |  | 252.1 | 
8 |  | 2.0 |  | 0.8 |  | 252.9 | 
9 |  |  | 1.5 | 0.5 |  | 253.4 | BM
2. Rise and Fall Method:

## Slide 7
Collimation Error
Surveying equipment receives continuous and often brutal use on construction sites. Therefore, it should be frequently tested and, if necessary, adjusted.
Collimation error occurs if the line of sight is not truly horizontal when the tubular bubble is centered, i.e. the line of sight is inclined up or down from the horizontal.
A check, known as two-peg test, is used to find this error as it was done in Surveying LAB- 5.
For instrument set up midway
between two pegs A and B:
)

## Slide 8
Since the instrument is at the same distance from both two points, error, e, is equal and cancel out.
For instrument set up at C and in the line of AB:
Sub (1) into (2):
e is in mm/m
If )e( is (+); line of sight is down, vise versa.

## Slide 9
Curvature Correction
The earth is being spheroid. Observations cannot be taken along this curved surface. A level generates a horizontal surface.
The line of sight is horizontal line (XB”) and level surface is defined as curvature correction.
As C is very small compared with R,
may be ignored.
where;
: , and
D: distance, km.

## Slide 10
Refraction Correction
In practice the staff reading would not be at B” but at Y due to refraction of the line of sight through the atmosphere. In general it is considered that the effect is to bend the line of sight down reducing the effect of curvature by 1/7th. Thus the combined effect of curvature and refraction is as follows:
Corrected Staff Reading = Staff reading
= Staff reading

## Slide 11
Example (5)
Calculate the error due to curvature and refraction for the following distances: a) 10m, b) 122m, c) 500m, and d) 1000m. Discuss your results.