## Slide 1: SURVEYING CHAPTER- 4 / PROFILE LEVELING-2
Asst. Lect. Ali Khalid
Al-Mansour University College
Civil Engineering Department
Second Year/ 2015-2016

## Slide 2
Example 7
The table below represents elevations of 7 stations for a proposed highway:
The cut depth at station (7+600) is 0.2 m. if you know that the slope of the proposed road is 1% upward from first to fourth station and 2% downward from fourth to last station, calculate cut and fill depths for the other stations with sketches.
Sol:
80.02 – Grade (7+600) = 0.2 -> -> Grade (7+600) = 79.82
Next Grade = Preceding Grade Slope distance
Grade (7+600) = Grade ( 7+400) + S * d
79.82 = Grade (7+400) + 0.01 * 200 -> -> Grade (7+400) = 77.82
Station, km | 7+000 | 7+200 | 7+400 | 7+600 | 7+800 | 8+000 | 8+200
Elevation, m | 73.03 | 75.12 | 78.41 | 80.02 | 75.67 | 72.09 | 69.13

## Slide 3
Station | Distance | Ground | Grade | Cut | Fill
7+000 | 0 | 73.03 | 73.82 | 0 | 0.79
7+200 | 200 | 75.12 | 75.82 | 0 | 0.7
7+400 | 200 | 78.41 | 77.82 | 0.59 | 0
7+600 | 200 | 80.02 | 79.82 | 0.2 | 0
7+800 | 200 | 75.67 | 75.82 | 0 | 0.15
8+000 | 200 | 72.09 | 71.82 | 0.27 | 0
8+200 | 200 | 69.13 | 67.82 | 1.31 | 0

## Slide 4
Chart: Profile of the Highway
| 0 | 200 | 400 | 600 | 800 | 1000 | 1200
Grade Elevation | 73.82 | 75.82 | 77.82 | 79.82 | 75.82 | 71.82 | 67.82
Ground Elevation | 73.03 | 75.12 | 78.41 | 80.02 | 75.67 | 72.09 | 69.13