## Slide 1: SURVEYING CHAPTER- 4 / PROFILE LEVELING-2
Asst. Lect. Ali Khalid
Al-Mansour University College
Civil Engineering Department
Second Year/ 2015-2016

## Slide 2
Example 8 (Homework)
The table below represents elevations of 6 stations for a proposed canal:
The fill depth at station (0+00) and (0+500) are 0.93 m and 0.11, respectively. Calculate cut and fill depths for the other stations with sketches.
Sol:
Station, km | 0+00 | 0+100 | 0+200 | 0+300 | 0+400 | 0+500
Elevation, m | 10.30 | 11.47 | 9.75 | 8.28 | 10.5 | 11.02

## Slide 3
Station | Distance | Ground | Grade | Cut | Fill
0+00 | 0 | 10.3 | 11.23 | 0 | 0.93
0+100 | 100 | 11.47 | 11.21 | 0.26 | 0
0+200 | 100 | 9.75 | 11.19 | 0 | 1.44
0+300 | 100 | 8.28 | 11.17 | 0 | 2.89
0+400 | 100 | 10.5 | 11.15 | 0 | 0.65
0+500 | 100 | 11.02 | 11.13 | 0 | 0.11

## Slide 4
Chart: Profile of the highway
| 0 | 100 | 200 | 300 | 400 | 500
Grade Elevation | 11.23 | 11.21 | 11.19 | 11.17 | 11.15 | 11.13
Ground Elevation | 10.3 | 11.47 | 9.75 | 8.28 | 10.5 | 11.02

## Slide 5
Example 9 (Homework)
The following set of readings was taken along stations of a proposed oil pipeline: 1.5, 1.52, 1.8, 1.9, 2.5, 3.02, 2.09, 2.47, 4.03, 2.55, 2.11, 3.22, and 3.1. The sixth reading was taken at a benchmark of 14 m next to fifth station and the instrument was shifted after third station and eight reading. The distance between each two stations (from 1 to 5) is 100 m; from 5 to 9 is 50 m and distance at station 10 is 0+620 km. Oil pipeline has to be constructed with the same elevation at station (0+620) and with no slope. Calculate cut and fill depths and draw the pipeline profile assuming suitable vertical and horizontal scales.