## Slide 1: SURVEYING CHAPTER- 5 / TRAVERSE AND TRAVERSING-1
Asst. Lect. Ali Khalid
Al-Mansour University College
Civil Engineering Department
Second Year/ 2015-2016

## Slide 2
Angles and Directions
Determining the locations of points and orientations of lines frequently depends on the observation of angles and directions. In surveying, directions are given by azimuths and bearings.
Methods of computing bearings and azimuths are based on:
1. Reference or starting line.
This line is called meridian.
2. Direction of turning.
If it is to right (clockwise: +)
or to the left (counterclockwise: -).
3. Angular distance (value of the angle).
Angles are most often directly observed
in the field with theodolite or total station instruments.

## Slide 3
Types of Meridian
Different meridians are used for specifying directions such as true, magnetic, and assumed meridian.
True or astronomical meridian: is the north-south reference line that passes through a mean position of the Earth’s geographic poles.
Magnetic meridian: is defined by a freely suspended magnetic needle that is only influenced by the Earth’s magnetic field.
True or astronomical meridian Magnetic meridian

## Slide 4
Assumed Meridian
An assumed meridian is an arbitrary direction assigned to some line in the survey from which all other lines are referenced. This could be a line between two property monuments, the centerline of a tangent piece of roadway, or even the line between two points set for that purpose.
The important point to remember about assumed meridians is that they have no relationship to any other meridian and thus the survey cannot be readily (if at all) related to other surveys. Also, if the original monuments are disturbed, the direction may not be reproducible.
It is good practice when assuming a direction to avoid directions that might appear to be true. If assuming a direction on a line that runs generally north and south, do not assume a north direction, as some future surveyor may mistakenly use your direction as true.

## Slide 5
Types of Angles
Horizontal angles most commonly observed in surveying are:
1. Interior angles: located inside a closed polygon.
2. Exterior angles: located outside a closed polygon.
3. Deflection angles: are observed from an extension of the back line to the forward station.
interior angles + exterior angles = 360⁰
The advantage to be gained by observing them is their use as another check.

## Slide 6
3. Deflection angles
Deflection angles may be observed to the right (clockwise: +) or to the left (counterclockwise: -).
Deflection angles are always smaller than 180°.
They are used principally on
the long linear alignments of
route surveys.
Note:
If the angle α > 360° then
α - 360°
If α is in (-) then
α + 360°

## Slide 7
Azimuths
Azimuths are horizontal angles observed clockwise from any reference meridian (True, magnetic, assumed, etc).
In plane surveying, azimuths are generally observed from north.
Azimuths may have readings between 0⁰ and 360⁰ degrees.

## Slide 8
Back Azimuths
The back azimuth of a line is the azimuth the line running in the reverse direction.
Back azimuth = azimuth 180⁰
For example:
= 68°
Back =
= 180⁰
= 68° + 180⁰ = 248⁰
If = 235° Back azimuth of AB =
- 180⁰ = 235° - 180° = 55°.