## Slide 1: SURVEYING CHAPTER- 5 / TRAVERSE AND TRAVERSING-1
Asst. Lect. Ali Khalid
Al-Mansour University College
Civil Engineering Department
Second Year/ 2015-2016

## Slide 2
Computing Azimuths
Azimuths of lines can be computed from interior angles as follow:
For clockwise direction use (-)
counterclockwise use (+).
For example:
Work direction is counterclockwise
Use (+) as follows:

## Slide 3
Example 1
Line | Azimuth
AB | 
BC | 
CD | 
DE | 
EF | 

## Slide 4
Azimuths of lines can be also computed from deflection angles as follow:
Deflection to the right (clockwise) use (+)
To the left (counterclockwise) use (-).
For example:
Deflection angle is to the right
Use (+) as follows:
Note:For exterior angle, convert it to interior angle and then solve.
285⁰ 20’
93⁰ 13’

## Slide 5
Example 2
Line | Azimuth
AB | 
BC | 
CD | 
DE | 
EF | 

## Slide 6
Bearings
The bearing of a line also gives the direction of a line with respect to the reference meridian.
The angle is observed from either the north or south toward the east or west.
Bearing may have values reading smaller than 90°.

## Slide 7
Back Bearings
The back bearing of a line is the bearing the line running in the reverse direction.
The back bearing can be obtained by changing:
1. the first letter from N to S or from S to N, and
2. the second letter from E to W or from W to E.
For example:
Back bearing of AB is
If = S 50° W

## Slide 8
Relation between Bearing and Azimuths
To simplify computations based on survey data, bearings may be converted to azimuths or azimuths to bearings.
N.E. Quadrant:
Bearing equals Azimuth
S.E. Quadrant:
180° -Azimuth = Bearing
180° - Bearing = Azimuth
S.W. Quadrant:
Azimuth - 180° = Bearing
Bearing + 180° = Azimuth
N.W. Quadrant:
360° -Azimuth = Bearing
360° - Bearing = Azimuth

## Slide 9
Example 3 (Homework)
Make a comparison between azimuth and bearing directions.
Example 4 (Homework)
Convert azimuths in (Page- 7) to bearings.
Example 5 (Homework)
Convert bearings in (Page- 13) to azimuths.
Example 6 (Homework)
Fill the blanks in the table below using the given figure shown.
Line | Azimuth | Bearing
AB |  | 
BC |  | 
CD |  | 
DE |  | 
EA |  |