## Slide 1: SURVEYING CHAPTER- 5 / TRAVERSE AND TRAVERSING- 3
Asst. Lect. Ali Khalid
Al-Mansour University College
Civil Engineering Department
Second Year/ 2015-2016

## Slide 2
Polygon closed traverse
For polygon traverse, standard sum of interior angles is given by:
Sum = (n – 2) * 180⁰
where n is the number of angles.
For example:
Triangle | Parallelogram
Sum = (3-1) * 180⁰ = 180⁰ | Sum = (4-1) * 180⁰ = 360⁰

## Slide 3
Example 9
For the given polygon shown, correct the interior angles if necessary.
A
B
C
D
85⁰ 20’
110⁰ 30’
98⁰ 10’
66⁰ 20’

## Slide 4
Example 10 (Homework)
For the given polygon shown, correct the interior angles if necessary.
A
B
C
D
85⁰ 20’
110⁰ 30’
98⁰ 10’
66⁰ 21’

## Slide 5
Angle Misclosure Error
If no standards are given, assume:
where is theodolite accuracy
Example 11
For 5 line traverse, the sum of interior angles is 538⁰ 40’ and the instrument accuracy is 10’. Do you accept the observations?

## Slide 6
Linear Misclosure Error
Large linear misclosure certainly indicate that either significant errors or even mistakes exist. Small linear misclosure usually mean the observed data are precise and free of mistakes, but it is not a guarantee that systematic or compensating errors do not exist.
dep.
lat.
Typical precision: 1/5000 for rural land, 1/7500 for suburban land, and 1/10,000 for urban land.

## Slide 7
Balancing a polygon traverse
There are several methods for balancing coordinates. Compass Rule will be adopted.
The Compass Rule is used when the accuracy of angular measurement is about equal to the accuracy of distance measurement.
This method works well for an EDM-theodolite traverse and total station.
where
L: length of line to be corrected, m, and
: sum of polygon traverse length, m.