## Slide 1
Structural Steel Design
Al Mansour University College
Civil Engineering Department
4th year
Asst. Lect. Haider Qais
Lecture 1

## Slide 2
STRUCTURAL DESIGN:
Structural design of buildings or other structures should be carried out as per the relevant code of practice.
Structural concrete Design shall conform to ACI code.
Structural steel design and fabrication shall conform to AISC manual planes.

## Slide 3
Types of steel structures:
1- Buildings - public buildings
- industrial buildings
- residential buildings
2- Bridges - rail roads
- mono rail (overground)
- highwys & pedestrins
3- Other structures
- power trnsmision towers, for
- radars & t.v installiations
- water supply tanks.
- ships & air planes.

## Slide 4
Steel material types:
- Carbon steel [0.2% to 1.5% carbon] + Fe (A36, A53, A500, A501, A529, A570), ideal type for structural applications because of cheap production
cost and high ductility
- Low carbon steel [~ 0.2% carbon] uses: sheets, wires, pipes, rebar
- Mild carbon steel [0.3% to 0.7% carbon] uses: rails, boilers, plates, axles,
structures.
- High Carbon Steel [0.7% to 1.5% carbon] Uses: Surgical instruments, razor blades, cutlery, spring, construction.

## Slide 5
Advantages of steel as structural material:
High strength:
The high strength of steel per unit of weight means that the weight of structures will be small
This fact is important for: long span bridges, tall buildings, and structures situated on poor foundations.
Uniformity
The properties of steel do not change with time, as do those of reinforced concrete structures.
Elasticity
Steel behaves closer to design assumptions
The moment of inertia of a steel structure can be accurately calculated.
Ductility
The property of a material by which it can withstand extensive deformation without failure under high tensile stress is its ductility.
It gives warning before failure take place.
Toughness
Steel has both strength and ductility.
A steel member loaded until it has larger deformations will still be able to withstand large forces. For example, steel member can be subjected to larger deformation during fabrication without fracture (steel member can be bend, hammered, sheared, and holes punched)

## Slide 6
Disadvantages of steel as a structural material:
1. Maintenance cost
Steel structures are disposed to corrosion when exposed to air, water, and humidity. They must be painted periodically.
2. Fireproof cost
The strength of steel members is reduced at high temperatures.
3. Buckling
For most structures the use of steel columns is very economical because of their high strength to weight ratio. However, as the length and the slenderness of a compression member is increased its danger of buckling increases.
4. Fatigue
The strength of structural steel member can be reduced if this member is subjected to cyclic loading.

## Slide 7
Some types of steel structures:
Steel structures can be divided into three general categories:
1. Framed structures: for example ( multistory buildings and bridges) Framed structures usually consist of beams, columns, and diagonal
bracing to provide stability.
2. Shell structures: for example water tanks
3. Suspension structures: for example (suspension bridges, and cable state bridges