## Slide 1
Structural Steel Design
Al Mansour University College
Civil Engineering Department
4th year
Asst. Lect. Haider Qais
Lecture 10

## Slide 5
Ex. Determine the LRFD and ASD design allowable strength for 2-MC12X40 (A36 steel) and 7/8 in bolts. Including the block shear in your calculation.
(Ans; 764.64k LRFD and 508.74 ASD)
Ex. The 6 X 4 X ½ angle shown has one line of ¾ Diameter of bolt in each leg, The bolt are 4in on center in each line and are staggered 2in respect to each other.
Ans 3.97in2
Extra Examples

## Slide 6
Ex . For the end truss shown in below calculate the applied load (p) on cantilever tip controlled by maximum strength or allowable capacity on net area of inclined truss element (2L4x4x3/8) only. Use A992G50 steel material, neglect the block shear.
(Ans; 57.15k LRFD and 38.1 ASD)

## Slide 7
BUILT UP TENSION MEMBERS
AISC Commentary- Part 16.1 / Sec. D4
They are tension members consist of 2 or more single members in separate or continuous contact with each other.
Components of a built-up tension member should be connected at frequent intervals to ensure that they act together, that faying surfaces intended to be in contact stay in contact, that excessive vibration of relatively thin parts does not occur, and that moisture will not penetrate between faying surfaces and cause corrosion.
So in continuous contact, S is the spacing between those elements ≤ 24 t of thinner thickness. Or 12” if the member is painted or not subjected to corrosion causes.
And in continuous contact, S should be ≤ 14 t of the thinner thickness or 7” when the member is not painted or subjected to corrosion causes.
For tension member built of separate elements, the elements should be connected by plates or other steel shapes in interval that the slenderness ratio of individual shape not exceed 300.
Provisions for

## Slide 8
lacing and tie plates, perforated cover plates, and fasteners, except those provisions intended specifically for compression members, are the same as for built-up compression members.
The design strength and allowable stresses for prismatic built-up members subjected to axial tension by static forces are the same as for tension members, so the strength should be computed as the sum of strength of members ( Tn = Σ Tni ).
The elements of built up section in tension should be connected @ ends & middle by tie plates with dimensions as follow:
- The length of tie plate (Ltp) should be ≥ (2/3) distance between connectors & it is
preferable to be same as width of built up members.
- The thickness of tie plate should be ≥ (1/ 50) Ltp.