## Slide 1
Structural Steel Design
Al Mansour University College
Civil Engineering Department
4th year
Asst. Lect. Haider Qais
Lecture 2

## Slide 2
Steel sections:
Notes:
W27x117: is a W section approximately 27 in deep weighing 117 Ib/ft.
L6x6x1/2: is an equal leg angle, each leg is 6 in long and ½ in thick.

## Slide 3
Stress – strain relationship in structural steel:
Fu: Ultimate Stress, Fy: Yield Stress
Stress = P / A, Strain = ⧍L / L

## Slide 4
If a piece of ductile structural steel is subjected to a tensile force, it will begin to elongate. If the tensile force is increased at a constant rate, the amount of elongation will increase linearly within certain limits.
When a tensile stress reaches a value roughly equal to three fourths of the ultimate strength of the steel the elongation will begin to increase at grate rate without a corresponding increase in the stress
Structural steel is usually grouped into several major ASTM classifications. As shown in the table (2-3 and 2-4) in the AISC Manual.
Loads:
The most important and most difficult task forced by the structural engineer is the accurate estimation of the loads that may be applied to a structure during its life.
The next important task is to determine the worst possible combinations of these loads that might occur at one time.
The objective of a structural engineer is to design a structure that will be able to withstand all the loads to which it is subjected while serving its purpose throughout its intended life span.
Loads can be classified into three categories: dead loads, live loads, and environmental loads (e.g. Snow loads, Rain loads, Wind loads, and Earthquake loads)

## Slide 5
TYPES OF LOADS:
Dead loads.
Live Loads.
Wind Loads.
Impact Loads.
Fatigue.
Earthquake Loads.
Snow Loads.
Other Loads.
Dead Loads: are loads of constant magnitude that remain in one position. The weight of the structure (beams, columns, slabs, wall, finishing, plastering etc) is considered dead load as well as attachments to the structure such as: pipes, air-conditioning, heating ducts, roof and floor covering, etc.
Live loads: are loads that may change in position and magnitude. They are caused when a structure is occupied, used, and maintained
Live loads are different for different types of structures and vary with type of occupancy. For example, for a residential building, live load on floor is considered as 3 kN/m2 while for industrial structures or business centers live loads can be taken as 4 or 5kN/m2. These loads vary for different structures based on intended use.

## Slide 6
Example of live loads;
Weight of people.
Furniture.
Machinery & goods.
Dynamic forces resulting from moving loads.
Wind loads.
Forces resulting from temperature change.
Pressure of liquids.
Earthquakes.

## Slide 7
Snow loads: freshly fallen dry snow weight is about 5-6 psf. While the packed snow weight is about 10 psf. (Snow loads on roofs < snow weight on grounds.
Wind load: are horizontal loads on the building which are exerted on the surface area of the building on windward side. This load is calculated based on the wind zone which provides the maximum wind speed in the given zone. This can be obtained from the wind map of the location. This wind speed is converted into force based on the surface area and orientation of building. wind direction. Shape of the building is or structural member is also considered for calculation.
ROOF PRESSURE = 1.25 x WIND PRESSURE
q = 0.00265 V²
For building with sloping roofs; aero dynamic effect must be consider as follow
Wind pressure can be approximately calculated as
Where; (v) is speed of air in mile / hour. (q) is pressure per unit area

## Slide 8
Snow loads: freshly fallen dry snow weight is about 5-6 psf. While the packed snow weight is about 10 psf. (Snow loads on roofs < snow weight on grounds.
Wind load: are horizontal loads on the building which are exerted on the surface area of the building on windward side. This load is calculated based on the wind zone which provides the maximum wind speed in the given zone. This can be obtained from the wind map of the location. This wind speed is converted into force based on the surface area and orientation of building. wind direction. Shape of the building is or structural member is also considered for calculation.
ROOF PRESSURE = 1.25 x WIND PRESSURE
q = 0.00265 V²
For building with sloping roofs; aero dynamic effect must be consider as follow
Wind pressure can be approximately calculated as
Where; (v) is speed of air in mile / hour. (q) is pressure per unit area

## Slide 9
Impact load: The term impact refers to the dynamic effect of a suddenly applied load (e.g. trucks, vehicles)