## Slide 1
Structural Steel Design
Al Mansour University College
Civil Engineering Department
4th year
Asst. Lect. Haider Qais
Lecture 3

## Slide 2
Acceptable methods for designing structural steel member:
The AISC specification provides two acceptable methods for designing steel structural members and their connections, which are Load and Resistance Factor Design (LRFD) and Allowable Strength Design (ASD).
Both procedures are based on limit state design principles. The term limit state is used to describe a condition at which a structure or part of a structure ceases to perform its function. There are two categories of limit state: strength and serviceability
Strength limit states define load – carrying capacity including yielding, fracture, buckling, and fatigue.
Serviceability limit states define performance including deflection, cracking, and vibration.

## Slide 3
With both LRFD and ASD the term nominal strength is used. The nominal strength of a member is its calculated theoretical strength with no resistance factor (Ø Phi) or safety factor (Ω Omega) applied. A resistance factor usually less than 1.0 is multiplied by the nominal
strength of a member to account for variation in material strength, member dimensions and workmanship.
With both the LRFD and ASD procedures values of the individual loads (dead, live, wind, snow, etc.) are first estimated. These loads are referred to as service or working loads.
With the LRFD method, possible service load groups are formed and each service load is multiplied by a load factor, normally larger than
1.0. The result linear combination of service loads in a group, each multiplied by its respective load factor, is called factored load.

## Slide 4
LRFD
Ru or U = 1.4D
Ru or U = 1.2D + 1.6L + 0.5 (Lr or S or R)
Ru or U = 1.2D + 1.6(Lr or S or R) + (0.5L or 0.8W)
Ru or U = 1.2D + 1.6W + 0.5L + 0.5 (Lr or S or R)
Ru or U = 1.2D ± 1.0E+ 0.5 L + 0.2S
Ru or U = 0.9D ± (1.6W or 1.0E)
Ru or U ≤ n * Rn
ASD
Ru or U = D
Ru or U = D + L
Ru or U = D + (Lr or S or R)
Ru or U = D + 0.75L + 0.75 (Lr or S or R)
Ru or U = D ± (W or 0.7E)
Ru or U = D ± 0.75(W or 0.7E) + 0.75 L + 0.75 (Lr or S or R)
Ru or U = 0.6D ± (W or 0.7E)
Ru or U ≤* Rn/ Ω
Where:
U = the design or ultimate load
D = dead load
L = live load due to occupancy
Lr = roof live load
S = snow load
R = nominal load due to initial rainwater or ice
W = wind load
E = Earthquake load
Load calculations (Computing combined loads)

## Slide 5
Specifications for design of steel structures:
Many available standards for properties & specifications of steel sections may be followed in design & constructions are published by some institutes & associations such as:
AISC: American institute of steel construction.
AASHTO: American association of state highway & transportation officials.
AISI: American Iron & Steel Institute.
AREA: American Railway Engineering Association.
ASTM: American Society for Testing& Material.
NBC: National Building Code.
UBC: Uniform Building Code.
BS: British Standard.
DIN: Dutch International Norma.
FIP: French International
EURO: Euro Code.

## Slide 6
American Institute of Steel Construction (AISC), Inc. publishes the AISC Manual of Steel Construction (Steel construction manual, or SCM), which is currently in its 13th edition. Structural engineers use this manual in analyzing, and designing various steel structures. Some of the chapters of the book are as follows:
Part1- Dimensions and properties of various types of steel sections available on the market (W, S, C, WT, HSS, etc.).
Part 2- General design considerations.
Part 3- Design of flexural members.
Part 4- Design of compression members.
Part 5- Design of tension members.
Part 6- Design of members subject to combined loading.
Part 7- Design consideration for bolts.
Part 8- Design considerations for welds.
Part 9- Design of connecting elements.
Part 10- Design of simple shear connections.
Part 11- Design of flexure moment connections.
Part 12- Design of fully restrained (FR) moment connections.
Part 13- Design of bracing connections and truss connections.
Part 14- Design of beam bearing plates, column base plates, anchor rods, and column splices.

## Slide 7
Part 15- Design of hanger connections, bracket plates, and crane-rail connections.
Part 16- General nomenclature.
Part 17- Specifications and codes.
-Commentary on specifications and codes.
-Miscellaneous data and mathematical information.

## Slide 8
Types of structural steel elements:
According to product method, we have two types as follow:
Standard hot rolled steel shapes:
They are formed from hot billet steel by passing through rolls numerous times to obtain the shape required.
The steel manual refer to the hot rolled steel shapes as follow:
Wide flange steel shape referred by WF as W 27x117
This steel shape is the most common structural steel section.
Standard steel shape referred by S as S 12x30
This has a thick web & narrow flange compared to W steel shapes.
Standard channels referred by C as C 10x30 or MC 18x58.
The second type referee to miscellaneous channels shapes which can not be classified with C shapes category.
Structural tee shapes refereed by WT as WT 18x58 or ST as 18x60.
In which WT is T-shape cut from W shape & ST is T-shape cut from S shape.
Angles refereed by L as L 4x4x1/2 & they are categorized as equal & non equals legs angles.