## Slide 1
Structural Steel Design
Al Mansour University College
Civil Engineering Department
4th year
Asst. Lect. Haider Qais
Lecture 4

## Slide 2
Analysis of Tension Members
Tension members are structural elements that subjected to axial tensile forces, such as:
Members in trusses
Cables in cable-stayed and suspension bridges
Bracing in frames to resist lateral forces from blast, wind, and earthquake.
In the early days of steel structures, tension members consisted of rods, bars, and perhaps cables. Today tension members usually consist of single angles, double angles, tees, channels, W sections, or suctions built up from plates or rolled shapes. Another type of tension section often used is the welded tension plate, or flat bar, which is very satisfactory for use in transmission towers, signs, foot bridges.

## Slide 3
Nominal strength of tension member:
A ductile steel member without holes and subjected to a tensile load can resist without fracture a load larger than its gross-sectional area times its yielding stress.
If, on the other hand, we have a tension member with bolt holes, it can possibly fail by fracture at the net section through the holes. This failure load may very well be smaller than the load required to yield the gross section, apart from the hole.
As a result of the preceding information, the AISC specification D2 states that the nominal strength of a section of a tension member, Pn, is to be the smaller of the values obtained by substituting into the following two expressions:

## Slide 4
for the limit state of yielding in the gross section (which is needed to prevent excessive elongation of the member)
Pn = Fy * Ag (AISC equation D2-1)
ntPn = nt * Fy * Ag (nt=0.9 for the LRFD and Ωt = 1.67 for ASD)
For tensile rupture in the net section, as where bolt or rivet holes are present
Pn = Fu * Ae (AISC equation D2-2)
ntPn = nt * Fu * Ae (nt=0.75 for the LRFD and Ωt = 2 for ASD)
Where:
  Ag = gross area of member, in2 (mm2)
  Ae = effective net area, in2 (mm2)
    For Bolted connections: Ae = U x An
    For welded connection: Ae = U x Ag
  Fy = specified minimum yield stress, ksi (MPa)
  Fu = specified minimum tensile strength, ksi (MPa)
Values of Fy and Fu are provided in table 2-3 and 2-4 in the AISC manual for the ASTM structural steels on the market today

## Slide 5
Gross and Net area determination:
Gross area: the gross area of a member is the total cross-sectional area.
Net area: the net area of a member is the products of the thickness and the net width of each element computed as follows:
In computing net area for tension and shear, the width of a bolt hole shall be taken as 1/16 in greater than the nominal dimension of the hole (or the width of the bolt hole = the value from table J3.3 + 1/16).
For a chain of holes extending across a part in any diagonal or zigzag line, the net width of the part shall be obtained by deducting from the gross width the sum of the diameters or slot dimensions of all holes in the chain and adding, for each gage space in the chain, the quantity

## Slide 6
S2 /4g
  S = longitudinal center to center spacing (pitch) of any two
consecutive holes, in.
g = transverse center to center spacing (gage) between fastener gage lines, in.
In determining the net area across plug or slot welds, the weld metal shall not be considered as adding to the net area.
Section J4.1 (b) limits An to a maximum of 0.85 Ag for splice plates
OR wn = wg – Σ (D+1/8) + n s² / 4g.

## Slide 7
BASES OF DESIGN:
Design is process by which an optimum solution should be obtained.
The typical criteria are:
Min cost.
Min weight.
Min construction time.
Min labours.
Max efficiency.
Serve the function wanted.
Long life.