## Slide 1
Structural Steel Design
Al Mansour University College
Civil Engineering Department
4th year
Asst. Lect. Haider Qais
Lecture 5

## Slide 2
Example 1:
Determine the net area of the (3/8 x 8- in) plate shown in the figure below. The plate is connected at its end with two lines of (3/4 - in) standard bolts.
Solution
Ag in2
An = 3-2*( =2.34375
= 2.34 in2

## Slide 3
Example 2:
Determine the critical net area of the (1/2 in) thick plate shown in the figure below. The standard holes are punched for (3/4 in) bolts.
Solution
Ag =1/2 * 11 = 5.5in2
An (ABCD) = 5.5-2*(1316+116)*12 =4.625 in2
An (ABEF) = 5.5-2*(1316+116)*12+324*6*12 =4.8125 in2
An (ABCEF) = 5.5-3*(1316+116)*12+324*3*12 =4.5625in2 (controls)

## Slide 4
Example 3:
Determine the net area of the W12x16 shown in the figure below. Assume
that the standard holes are for 1 in bolts.
Solution
From the AISC manual For W 12x16: Ag = 4.71 in2, tw = 0.22 in
An (ABDE) = 4.71-2*(1116+116)*0.22=4.215 in2
An (ABCDE) = 4.71-2*(1116+116)*0.22+2*224*3*0.22 =4.1142 in2 (controls)

## Slide 5
Example 4:
Determine the net area along route ABCDEF for the C 15x33.9 shown in the figure below. Assume that the standard holes are for 3/4 in bolts.
Solution
From AISC manual For C 15x33.9: Ag = 10 in2, tw = 0.4 in, tf = 0.65 in
An (ABCDEF) = 10-2*( =8.77 in2