## Slide 1
Structural Steel Design
Al Mansour University College
Civil Engineering Department
4th year
Asst. Lect. Haider Qais
Lecture 6

## Slide 2
Effective net area:
When a member other than a flat plate or bar is loaded in axial tension until failure occurs across its net section, its actual tensile failure stress will probably be less that the tensile strength of the steel, unless all of the various elements which make up the section are connected so that stress is transferred uniformly across the section
                If the forces are not transferred uniformly across a member cross section, there will be a transition region of uneven stress running from the connection out into the member for some distance. An angle section having connection to one leg only is an example of such a case

## Slide 3
To account for the non-uniformity, the effective net area of tension member shall be determined as follows:
Ae = An U (AISC equation D3-1)
U = the shear leg factor, is determined as shown in table D3.1
The above equation logically applies for both fastener connections having holes and for welded connections.
For welded connections, the net area equal the gross area since there are no hole
Whenever the tensile load is transmitted by bolts, rivets, or welds through some but not all of the cross-sectional elements of the members, the load carrying efficiency is reduced and U will be less than (1)

## Slide 4
For bolted member: the following equation can be used to estimate the shear leg factor or reduction coefficient U
= Distance from the plain of the connection to the centroid of the area of the whole section
L = length between first and last bolts in the line. When there are two or more lines of bolts, L is the length of the line with the maximum number of bolts.
In order to calculate U for W section connected by its flange only, we will assume that the section is split into two structural tees. Then the will be the distance from the outside edge of the flange to the C.G of the structure Tee
For welded members: when tension loads are transferred by welds, the rules from AISC table D3.1 that are to be used to determine values of A and U are as follows
1. Should the load be transmitted only by longitudinal welds to other than a plate member, or by longitudinal welds in combination with transverse welds, A is to equal the gross area of the member Ag.
2. Should a tension load be transmitted only by transverse welds, A is to equal the area of the directly connected elements U is to equal 1.0 (case 3 in Table D3.1)
3. Test has shown that when flat plates or bars connected by longitudinal fillet welds are used as tension members, they may fail prematurely by shear lag at the corners if the welds are too far apart. Therefore, the AISC specification states that when such situations are encountered, the length of the welds may not be less than the width of the plates or bars. The letter A represents the area of the plate, and UA is the effective net area. For such situations the value of U to be used (case 4 in Table D3.1) are as follows:

## Slide 5
When l ≥ 2w (U = 1.0)
When 2w≥ l ≥ 1.5w (U = 0.87)
When 1.5w≥ l ≥ w (U = 0.75)
Where
l = weld length, in
w = plat width (distance between weld), in
Connecting elements for tension members: when splice or gusset
plates are used as statically loaded tensile connecting elements, their strength shall be determined as follows

## Slide 6
Example 5:
Determine the LRFD tensile design strength for a W 10x45 with two lines of (3/4in diameter) bolts in each flange using A572 Grade 50 steel and the AISC specification. There are assumed to be at least three bolts in each line (4in on center), and the bolts are not staggered with respect to each other.

## Slide 7
Solution
From table 2-6 of AISC manual Fy = 50 ksi, Fu = 65 ksi for A572 Grade 50 steel.
From table 1-1 (W shapes Dimensions): for W 10x45 (Ag = 13.3 in2, d =
10.1 in, bf = 8.02 in, tf = 0.62 in)
Cross sectional yielding
Pn = FyAg
Pn = 50 * 13.3 = 665k
ntPn = nt * Fy * Ag
0.9*665 = 598.5k
Tensile rupture strength
An = 13.3 – 4* (1316+116)*0.062=11.13 in2
L = 4 + 4 = 8in
U = 1- /L
= 1-0.907/8 = 0.8866
bf = 8.02in > (2/3)d =(2/3)10.1 = 6.7333in
U = 0.9 from table (D3-1 case 7) ….. control
Ae=UAn
= 0.9 * 11.13 = 10.017in2
Pn = Fu Ae
= 65 * 10.017 = 651.105k
ntPn = nt * Fu * Ae
= 0.75 * 651.105 = 488.3588k ….. (Control)
From table 1-8 (WT shapes Dimensions): for WT 5x22.5 (which is half of a W10x45) = 0.907