## Slide 1
Structural Steel Design
Al Mansour University College
Civil Engineering Department
4th year
Asst. Lect. Haider Qais
Lecture 7

## Slide 2
Example 6
Determine the LRFD design tensile strength for an A36 L6x6x3/8 in that is connected at its ends with one line of four (7/8in) diameter bolts in standard holes (3in) on center in one leg of the angle.

## Slide 3
Solution
From table 2-6: Fy =36 ksi, Fu = 58 ksi for A36 steel.
From table 1-7 (L shapes dimensions): Ag = 4.38in2, = = 1.62in
Cross sectional yielding
Pn = FyAg
Pn = 36 * 4.38 = 157.68k
ntPn = nt * Fy * Ag
0.9*157.68 = 141.912k ….. (control)
Tensile rupture strength
An = 4.38 – (1516+116)*38=4.005 in2
L 3+3+3 = 9in
U = 1- /L
= 1- 1.62/9 = 0.82 (control)
𝑈 = 0.8 (𝑓𝑟𝑜𝑚 𝑡𝑎𝑏𝑙𝑒 𝐷3 − 1 𝑐𝑎𝑠𝑒 8)
Ae=UAn
= 0.82 * 4.005 = 3.2841in2
Pn = Fu Ae
= 58 * 3.2841= 190.4778 k
ntPn = nt * Fu * Ae
= 0.75 * 190.4778 = 142.8584

## Slide 4
Example 7
The 1x6 in plate shown in the figure below is connected to a 1x10 in plate with longitudinal fillet welds to transfer a tensile load. Determine the LRFD tensile design strength of the member if Fy = 50 ksi and Fu = 65 ksi.

## Slide 5
Solution
Considering the nominal or available tensile strength of the smaller plate 1x6 in:
Cross sectional yielding
Pn = FyAg
Pn = 50 * 1 * 6 = 300 k
ntPn = nt * Fy * Ag
0.9*300 = 270 k
Tensile rupture strength
An = Ag = 1 * 6 = 6 in2
1.5w = 1.5 * 6 = 9in
1.5w > L > w
9 > 8 > 6
U = 0.75 (from table D 3-1 case 4)
Ae = UAn = 0.75 *6 = 4.5 in2
Pn = Fu Ae
= 65 * 4.5= 292.5 k
ntPn = nt * Fu * Ae
= 0.75 * 292.5 = 219.375….. (Control)

## Slide 6
Example 8
Compute the LRFD design strength of the angle (8x6x3/4 in) shown in the figure below. It is welded on the ends and sides of the 8 in leg only. Fy = 50 ksi and Fu = 70 ksi.

## Slide 7
Solution
From table 1-7 (L shapes Dimensions): for L 8x6x3/4 (Ag = 9.99 in2 1.56in)
Cross sectional yielding
Pn = FyAg
Pn = 50 * 9.99 = 499.5 k
ntPn = nt * Fy * Ag
0.9*499.5 = 449.5 k
Tensile rupture strength
An = Ag = 9.99 in2 , L = 6in
U= 1- /L = (1-1.56/6) = 0.74
Ae = UAn = 0.74 *9.99 = 7.3926 in2
Pn = Fu Ae
= 70 * 7.3926= 517.48 k
ntPn = nt * Fu * Ae
= 0.75 * 517.48 = 388.11….. (Control)