## Slide 1
Structural Steel Design
Al Mansour University College
Civil Engineering Department
4th year
Asst. Lect. Haider Qais
Lecture 9

## Slide 2
Design of Tension Members
Selection of Members:
· This chapter deals with the design of tension members for external loads.
· In general the design of tension members should have the following properties:
1. Compactness
2. Dimensions that fit into the structure with reasonable relation to other member dimensions.
3. Connection to as many part of the section as possible to minimize shear block and leg

## Slide 3
The choice of member type is often affected by the type of connections used for the structure. Some steel section are not very convenient to bolt together with the required gusset or connection plates, while the same section may be welded together with little difficulty.
1. Tension members consisting of angles, channels, and W or S sections will probably be used when the connections are made with bolts
2. Plates, channels and structural tees might be used for welded structures.
· The slenderness ratio of a member is the ratio of its unsupported length to its least radius of gyration. For tension members other than rods, the maximum value of slenderness ratio is suggested to be 300 (section D.1 of the specification).the purpose of such limitation for tension members is to ensure the use of sections with stiffness sufficient to prevent undesirable deflections or vibrations.

## Slide 4
· The area needed for a particular tension member can be estimated with the LRFD or the ASD equations. If the LRFD equations are used, the design strength of a tension member is the least of Øt Fy Ag, Øt Fu Ae, or its block shear strength Øt Rn. in addition, the slenderness ratio should not exceed 300.
To satisfy the first of these expressions, the minimum gross area must be at least equal to
To satisfy the second of these expressions, the minimum value of Ae must be at least equal to:

## Slide 5
And since Ae = UAn for bolted,
And since Ag = Min An + estimated area of holes,
The third expression can be evaluated, once a trial shape has been selected and other parameters related to the block shear strength are known.
The designer can substitute into equations 1 and 2, taking the larger value of Ag so obtained for an initial size estimate.
The maximum preferable slenderness ratio L/r is 300. From this value, it is easy to compute the smallest preferable value of r.