## Slide 1: CE 405 Sanitary and Environmental Engineering
Al Mansour University College
Civil Engineering department
2017-2018
Lecture 2
Dr Ameer Badr Khudhair

## Slide 2: Population estimation
Design of water supply and sanitation scheme is based on the projected population of a particular city, estimated for the design period. Any underestimated value will make system inadequate for the purpose intended; similarly overestimated value will make it costly.
Forecasts are susceptible to error if for no other reason that nobody knows the future. Many methods are used to forecast the population in the future. Each method has it’s own assumptions:
Arithmetic method
Geometric method
Ratio method
Compound method
Saturation method

## Slide 3: Arithmetic method
Based on the past population data, this method works out an average arithmetic increment in population per time period and uses this increment to forecast the future population.
Assumption: The rate of change is constant (k)
Where:
𝑃𝑓: final population
𝑃𝑖: initial population
K: constant
∆t: period difference

## Slide 4
Example: The recent population of a city is 30,000 inhabitant. What is the predicted population after 30 years if the population increases 4000 in 5 years.
K = 4000/ 5 = 800 capita / year
= 54,000 capita

## Slide 5
Example: The past population of a city is given in table below, calculate the population in 2031. using Arithmetic method.
Population | Year
1,240,000 | 1981
1,510,000 | 1991
1,760,000 | 2001
2,025,000 | 2011
K | Population | Year
 | 1,240,000 | 1981
27,000 | 1,510,000 | 1991
25,000 | 1,760,000 | 2001
26,500 | 2,025,000 | 2011
K = (27,000+ 25,000 + 26,500)/3 = 26,167 capita / year
= 2,548,340 capita

## Slide 6: Example: A small community has a population of 1,000 and is growing by 1.5% each year. The ADD in the community is 500,000 L/day. The daily peaking factor is 2.75. What will be the ADD and MDD be after 20 years? use Arithmetic method.
Pf = Pi + K t
=1000+ (1.5*1000/100 )* 20= 1300 capita
Current ADD = 500,000/1000 =500 lpcd
Future ADD (community) = 500*1300 = 650,000 l/day
Future MDD (community) =650,000 *2.75 = 1,787,500 l/day

## Slide 7: Geometric method
This method is based on the assumption that percentage growth rate is constant.
ln Pf= ln Pi+ k. ∆t
Where:
ln: natural logarithm
𝑃𝑓: final population
𝑃𝑖: initial population
K: constant
∆t: period difference

## Slide 8
Example: The recent population of a city is 30,000 inhabitant. What is the predicted population after 30 years if the geometric growth rate is 0.035
ln Pf = ln Pi+ k. ∆t
ln = ln 30,000 + 0.035* 30
10.31 + 1.05
capita

## Slide 9
Example: Given the following information about the population of city. Estimate the population at 2030 using Geometric method.
population | year
62,000 | 2000
74,000 | 2005
85,000 | 2010
100,000 | 2015
? | 2030
K | population | year
 | 62,000 | 2000
0.0354 | 74,000 | 2005
0.0277 | 85,000 | 2010
0.0325 | 100,000 | 2015
K = (0.0354 + 0.0277 + 0.0325)/3 = 0.0319
= 161,365 capita

## Slide 10
HW: the past population of a city is given in table below, calculate the population in 2036. using Arithmetic and Geometric method.

## Slide 11: Ratio method
It is used to calculate the population of a small city in a big city. With similar growth rate.
=
Where:
𝑃𝑓R: number of future population for the area under study
𝑃𝑖R: number of population for the area under study
𝑃𝑓: number of future population for the whole area
𝑃𝑖: number of population for the whole area

## Slide 12: Example: The population of a city A in 1990 was 51000 capita. Estimate the population of city A in year 2025. The growth rate of city A is similar to city B.
City A |  | City B | 
Year | Pop. * 1000 | year | Pop. * 1000
1970 |  | 1970 | 69
1980 |  | 1980 | 80
1990 | 51 | 1990 | 93
2000 |  | 2000 | 110

## Slide 13
Solution
First calculate the growth rate of city B, then the population of city B in 2025
If did not mention in the question the method must use then choose the method you want, let say Arithmetic method
Growth rate (k1) = (80000-69000)/ (1980-1970) = 1100 c/y
K2= (93000-80000)/ (10) = 1300 c/y
K3= (110000-93000)/ (10) = 1700 c/y
Average K= 1367 c/y
P2025= P2000 + K.t
P2025= 110,000 + 1367 *25 = 144,175 c
Calculate the population of city A in 2015 by ratio method due similarity with city B
Pop (A) 2025 = 51,000* 144,175/93,000 = 79,064 c

## Slide 14: Compound method
It is the most accurate and complex method
Pf = Pi*
r= (b-d) + (i-o)
Where:
Pf :future population
Pi : present population
k : r/ Pi
t: time
b: birth rate
d: death rate
i: immigration to the city under study
o: immigration out of the city under study

## Slide 15: Example: In a City, the birth babies= 80 c/d, the death = 30 c/d, the immigration out of the city = 5 c/d, where is no immigration to the city. The population of the city in 2015 = 5,000,000. Calculate the population in 2020.
R = (80 -30) + ( 0- 5) = 45 c/d = 16,425 c/y
Unit of k must be (1/year), so divided by the population
k = 16,425/ 5,000,000 = 0.00328 1/y
Pf = Pi*e(k. Δ𝑡)
P2020 = 5,000,000 * e(0.00328 *5) = 5,082,676 capita

## Slide 16: Saturation method
In this method, the maximum possible density of population is estimated according to the number of apartments and stories per unit area and the maximum family members.
P= Pi + (S-Pi)(1-e-K.∆t )
Where:
P = population
t = time
k = decreasing rate of increase growth constant
S = Saturation population
Note: the saturation population is the maximum number of people can inhabit a town based on the physical constraints of buildable land zoning

## Slide 17: Example: City A has pop in 1990, 110,500 capita, in 2000 the population was 118200, assume Saturation limit for city A is 250000, K= 0.00568, calculate the population in 2025.
Solution
P = P1 + (S-P1)(1- e –K*Δt)
P2025 = 118200+ (250000-118200) (1-e-0.00568*25) =135648 capita

## Slide 18: Example: A city has 250,000 capita, the average daily demand is 220 lpcd, the factors 1.8 & 2.7 are used for Maximum daily demand and peak hourly demand. There are 2 building in the city each of 500 m2 with 3 stories, the fire would not extend more than 4 hours, calculate the total demand if the losses is 15%.

## Slide 19
Solution:
𝑄=4080√𝑝X(1−0.01√𝑝) = 4080* √250(1-0.01*√250) = 54,310 l/min
F= 18*C*√A = 18*1*√(500*3*2*3.282) = 3234 gal/min = 12,240 l/min
Both results are acceptable, I will use 54,310 l/min
It mentions the fire will not extend more than 4 hours, so
Fire requirement = 54,310 *(60*24) *(4/24) = 13,034,400 l/d
Maximum daily demand = average daily demand * factor
MDD = 220 * 250,000 * 1.8 = 99,000,000 L/d
PHD = 220 * 250,000 * 2.7 = 148,500,000 L/d
Losses =0.15 from the total
Total required by water treatment plant = (MDD + Fire requirement) * 1.15 = 128,839,560 l/d
Total required by distribution system = (PHD + Fire requirement) *1.15
= 185,764,560 L/d