## Slide 1: CE 405 Sanitary and Environmental Engineering
Al Mansour University College
Civil Engineering department
2017-2018
Lecture 3
Dr Ameer Badr Khudhair

## Slide 2: Pollution
Pollution is the introduction of a contaminants/ pollutants into the environment. It is created by industrial and commercial waste, agricultural practices, everyday human activities that cause adverse change to human health and environment.
Pollution can take the form of biological creatures, chemical substances or energy, such as noise, heat and radiation.

## Slide 3: The are three types of pollution:
Land Pollution
Air Pollution, Ex: London Great Smog 1952
Water Pollution, Ex: London Great Stink 1858

## Slide 4: Type of wastes according to its sources
Domestic waste: food residual, human waste, grease, oil, detergents.
Industrial waste: according to the industry such as petroleum from oil well.
Agricultural waste: mainly pesticide, herbicide
Hospital waste: mainly viruses, bacteria

## Slide 5: Waste source
Point Source: discharge of pollutants from single point. Factories, power plants, sewage treatment plants, oil wells.
Non-point Source: sources of water pollution that are scattered or diffuse, not having a specific location. Farm fields, cities, roads, clear-cut forests, mines.

## Slide 6: Water pollution
Water is considered polluted if some substances or condition is present to such a degree that the water cannot be used for a specific purpose.
Water pollution is the presence of excessive amounts of a hazard (pollutants) in water in such a way that it is no long suitable for drinking, bathing, cooking or other uses.
Physical, chemical, biological changes in water quality that adversely affect living organisms, human and environment.

## Slide 11: Types of water pollution
pH scale
Sediment (Particulates)
Thermal Pollution
Infectious Agents
Inorganic Pollutants
Organic Chemicals (non domestic waste)
Oxygen-Demanding Wastes (domestic waste)

## Slide 12: Acid and base
Affect the degree of corrosion of metals as well as disinfection efficiency
The pH of the water entering the distribution system must be controlled to minimize the corrosion of pipes in household water systems. Failure to do so can result in the contamination of drinking-water and in adverse effects on its taste, odor.

## Slide 13
pH is a way of expressing the hydrogen-ion concentration of a solution. As acids and bases in solution dissociate to yield hydrogen ions [H+] and hydroxyl ions [OH-] respectively, pH is used to indicate the intensity of the acidic or alkaline condition of a solution.
pH =-log[H]

## Slide 14
The alkalinity of water is its quantitative capacity to neutralize acids. The three major forms of alkalinity ranked in order of their association with high pH values are
(1) hydroxide [OH-]
(2) carbonate, [CO3-2]
(3) bicarbonate [HCO3-]

## Slide 15: Sediment
Sediment is the loose sand, clay, silt and other soil particles that settle at the bottom of a body of water.
Source: soil erosion and runoff, decomposition of plants and animals.
Cause: obstructs shipping channels, clogs pipes, purification more costly, disinfection process is not efficient.

## Slide 16
Turbidity is caused by suspended materials which absorb and scatter light, such as clay, silt, finely divided organic and inorganic matter, plankton and other microscopic organisms.
These materials are typically in the size range of 0.004 mm (clay) to 1.0 mm (sand). Turbidity can affect the color of the water.
These colloidal and finely dispersed turbidity-causing materials do not settle under quiescent conditions and are difficult to remove by sedimentation.
Turbidity is a key parameter in water supply engineering, because turbidity will both cause water to be unpleasant and cause problems in water treatment processes, such as filtration and disinfection.
Turbidity is also often used as indicative evidence of the possibility of bacteria being present.

## Slide 17
Thermal Pollution: an increase in water temperature
Source: Nuclear power plants, coal fried power plants, industrial effluents, domestic sewage.
Can cause: thermal shock

## Slide 18: Infectious Agents
Infectious Agents : pathogenic organisms. Water-borne diseases include typhoid, cholera, bacterial and amoebic dysentery, infectious hepatitis, guinea worm and bilharzia.
Due to lack of sanitation, analyze coliform bacteria (E. coli). Presume if coliform bacteria are present, infectious pathogens are also present.

## Slide 19
Some human diseases transmitted by polluted water

## Slide 20: Inorganic Pollutants
Inorganic Pollutants are caused mainly by human activities
Metals, like mercury, lead, tin, cadmium, selenium
Non metals like Arsenic
Another classification according to ions
Cations (+)
Anions (-)

## Slide 21
Mercury (Hg+2)Poisoning
Source:
Industry such as (fluorescent light bulbs), cement and steel
Coal-fired power plants,
Incineration,
Natural sources, such as volcanoes
Causes:
Damage to the nervous system
Development delays
kidney disorders

## Slide 22
Lead (Pb+2) poisoning
Source
Incineration, pipes, solder, gasoline
Causes:
Nervous system, anemia, abortion, Hearing loss & learning disabilities

## Slide 23
Non metal
Arsenic (As+3)
Source: Industries, mining, pesticides, ground water
Causes: anemia, cancer

## Slide 24: Organic Pollutants
Such as pesticides, solvents, pharmaceuticals, and industrial chemicals
In 1995, the United Nations Environment Programme Governing Council investigated. Initially the Convention recognized only 12 POPs for their adverse effects on human health and the environment, placing a global ban on these particularly harmful and toxic compounds and requiring its parties to take measures to eliminate or reduce the release of POPs in the environment. Such as Dioxin, PCB, DDT.
Since 2001, this list has been expanded to include certain polycyclic aromatic hydrocarbons (PAHs) and other compounds

## Slide 25
Dioxin : Stable; slow to degrade
Generated from : Burning wood, coal, oil, household trash, and chlorine bleaching of paper.
Causes : Damage the immune system, interfere with hormones and also cause cancer.

## Slide 26
Polychlorinated Biphenyl (PCBs) : stable, non-flammable, high boiling points; does not conduct electricity well. So used in electrical industries such as transformers and capacitors .
Accumulates in fat of animals
Causes: hormonal and reproductive disruptions, cancer.

## Slide 27
DDT : insecticide; stable and slow to degrade.
Paul Muller won the Nobel Prize in 1948 for developing it. Benefits: Controlled spread of malaria; Provided crop protection.
Cause: decreased mental function, male infertility, cancer

## Slide 28
Problems with DDT: DDT is not metabolized very rapidly by animals; instead, it is deposited and stored in the fatty tissues bioaccumulation.

## Slide 29: Oxygen-Demanding Wastes
Oxygen dissolved in water is indicator of water quality. 6 part per million (ppm) of O2 or more supports desirable aquatic life.
BOD: Biochemical oxygen demand : measures the amount of dissolved oxygen consumed by aquatic microorganisms.
Sewage or food wastes can cause an Oxygen sag, where few fish survive.

## Slide 30: Biochemical oxygen demand (BOD)
BOD is the amount of dissolved oxygen needed by aerobic biological organisms in a body of water to break down organic material present in a given water sample at certain temperature over a specific time period depending on temperature, nutrient concentrations, and the enzymes available to indigenous microbial populations.
The BOD value is most commonly expressed in milligrams of oxygen consumed per liter (mg/l) of sample during 5 days of incubation at 20 °C and is often used as a indicator of the degree of organic pollution of water and effectiveness of wastewater treatment plants.
BOD is similar in function to chemical oxygen demand (COD), in that both measure the amount of organic compounds in water. However, COD is less specific, since it measures everything that can be chemically oxidized, rather than just levels of biologically active organic matter.

## Slide 31
Most natural waters contain small quantities of organic compounds. Aquatic microorganisms have evolved to use some of these compounds as food.
Microorganisms living in oxygenated waters use dissolved oxygen to degrade the organic compounds, releasing energy and carbon source which are used for growth and reproduction. Populations of these microorganisms tend to increase in proportion to the amount of food available.
Under some circumstances, microbial can consume dissolved oxygen faster than atmospheric oxygen can dissolve into the water or the autotrophic community can produce.
Fish and aquatic insects may die when oxygen is depleted by microbial metabolism.

## Slide 32
Organic matter + O2+ bacteria CO2 + H2O + new cells of bacteria
Organic nitrogen + O2 + bacteria Ammonia-nitrogen
NH3-N +O2 Nitrate- nitrogen (NO3-N) ( nitrification)

## Slide 33
Dissolved oxygen (DO) depletion is most likely to become evident during the initial aquatic microbial population explosion in response to a large amount of organic material.
Most rivers will have a 5-day carbonaceous BOD below 1 mg/L.
Moderately polluted rivers may have a BOD value in the range of 2 to 8 mg/L.
Municipal sewage that is efficiently treated by a three-stage process would have a value of about 20 mg/L or less.
Untreated sewage varies, but averages around 600 mg/L in Europe and as low as 200 mg/L in the U.S., or where there is severe groundwater or surface water Infiltration/Inflow. The generally lower values in the U.S. derive from the much greater water use per capita than in other parts of the world.

## Slide 34: Typical values of k & BOD ultimate (L) for various waters for default temperature of 20°C

## Slide 35
)
Where:
: BOD at any time (mg/l)
: BOD ultimate (mg/l)
e: exponential
t: Time (day)
K: reaction constant (1/day), depend on temperature
ɵ = 1.135 for 4 < Temp ≤ 20°C
ɵ = 1.056 for Temp > 20°C

## Slide 36
BOD5 is calculated by:
Unseeded BOD5 =
Seeded BOD5 =
where:
is the dissolved oxygen (DO) of the diluted solution after preparation (mg/l)
is the DO of the diluted solution after 5 day incubation (mg/l)
is the decimal dilution factor
is the DO of diluted seed sample after preparation (mg/l)
is the DO of diluted seed sample after 5 day incubation (mg/l)
is the ratio of seed volume in dilution solution to seed volume in BOD test on seed
60- 70 % of the oxidation/ degradation of organic pollutants in 5 days
95- 99% oxidization in 20 days

## Slide 37
Example: determine BOD1 & BODu for waste water where BOD5 at 20˚C is 200 mg/l, k= 0.23 d-1

## Slide 38
Example: water sample has 0.02 dilution factor (1 ml from sample diluted in 50 ml distilled water), the initial dissolved oxygen (DO) is 10 mg/l, after 5 days the DO is 6 mg/l, calculate BOD5

## Slide 39
Thomas Graphical Method (McGhee 1991): This is an approximate method. It is based on the following equation:
Z= a + b. t
Where:
a: intercept with y axis
b: line slop (dy/dx)

## Slide 40
Sample calculation
Step 1: calculate (t/y)1/3

## Slide 41
step 2: Plot (t/y)1/3 versus “t” and found slope and intercept
Slope = 0.0205
Intercept = 0.8474
Step 3: From equations below obtained k and L
K = 2.61 = 0.063/day
L = = 11.34 mg/l

## Slide 42: HW: Compute the value of k & BODu for the data given below
Time (day) | BODt (mg/l)
2 | 11
4 | 13
6 | 22
8 | 24
10 | 26

## Slide 43: Treatment evaluation
Efficiency (BOD)
BOD: Biological oxygen demand
Inf: Influent (flow in)
Eff: Effluent (flow out)

## Slide 44
Example: the plant efficiency of treatment plant are 50% for BOD & 70% for suspended solid (SS), BOD & SS of wastewater enter the plant are 40 & 55 mg/l, respectively. Can we dispose the flowing out from the treatment plant to the river? Why?