## Slide 1: CE 405 Sanitary and Environmental Engineering
Al Mansour University College
Civil Engineering department
2017-2018
Lecture 4
Dr Ameer Badr Khudhair

## Slide 2: Water treatment plant
In the design of water treatment plants, the provision of safe water is the prime goal. Water treatment plants have demonstrated the ability to produce safe water under adverse conditions. They must also produce water which is appealing to the consumer. Ideally, appealing water is one that is clear and colorless, pleasant to the taste, and cool. It is non-staining, and is neither corrosive nor scale forming. The consumer is principally interested in the quality of water delivered to the tap in his home or place of business, as opposed to the quality at the treatment plant.

## Slide 3
Treatment process used depends on the raw water source and the quality of finished water desired. Many chemicals are employed in the treatment. The specific chemicals selected for treatment are based on their effectiveness to perform the desired reaction and cost. The most important consideration in designing water treatment plant is to provide flexibility.
Natural water polluted either by human activity or by nature, is likely to contain dissolved organic and inorganic substances; biological forms, such as bacteria and plankton; and suspended inorganic material.

## Slide 4: The principal water treatment unit processes employed to remove these substances are as follows:
Water resource
Intake
Rapid mixing
Coagulation and flocculation, Sedimentation
Filtration
Advanced treatment: Softening, Ion exchange, Adsorption, Reverse osmosis, Aeration.
Disinfection/ Chlorination
Ground storage
Water network system

## Slide 6: Intakes
Intakes are structures constructed in or adjacent to lakes, reservoirs, or rivers for the purpose of withdrawing water from the source to the water treatment plant. In general, they consist of an opening with a grate or strainer through which the water enters, and a conduit to conduct the water by gravity to a pumping station. The water is pumped from the pumping station to the water treatment facility. Schematic diagrams of lake and river intake systems are shown in Figures 1 and 2.

## Slide 7
Figure 1: tower intake in a lake (water surface).

## Slide 8
Figure 2: river intake.

## Slide 9: Type of Intake
Intake structures may be classified into two categories:
Direct intake: directly from the river.
Indirect intake: take from well beside the river.
Many varieties of these types have been used. The selection of the type of intake is highly dependent on local circumstances. Because the circumstances are fundamentally different, the systems are often classified as either river intakes or lake/reservoir intakes as shown in figure 1, 2.

## Slide 10: The key requirements of the intake structures are that they are:
Adequate size to provide the required quantity of water.
Located to obtain the best quality water.
Protected from objects that may damage equipment.
Easy to inspect and maintain.
Designed to minimize damage to aquatic life.
Located to minimize navigational hazards.

## Slide 11: Intake design elements
Water level variation: NPSH in site ≥ NPSH pump; NPSH: net positive suction head
Water quality: Use to remove objects to enter to system through strainer
Detention time in the well: range from 15-30 minutes, so the pumps do not work continuously.
Bottom of the well: the bottom of the well must reduce no more than 1 m from the river bottom.
The distance between the entrance pipe and the bottom of the well is almost 0.6 m

## Slide 12: Strainer design elements
Entrance velocity for strainers 0.15 - 0.3 m/s.
Area for strainer holes ≤ 50% of the gross area of the strainers.
Velocity for gravity pipe 0.6 -1.5 m/s.
Discharge for the washing pipe = 1/3 discharge for the gravity pipe.
Flow velocity for the washing pipe = 3 m/s.

## Slide 13
Example: It is required to design a strainer with imperforated top and 0.6 m height. Find the diameter of the gravity pipe, wash pipe and the size of the well if the flow required is 10 m3/min. The water surface elevation is 252 m, river bed elevation is 249 m.
Note: Use 2 units. Flow velocity (entrance to the strainer) = 0.15 m/s, gross area of strainer = twice effective area. Velocity in gravity pipe =1.5 m/s. Use Q for the washing pipe = 1/3 Q for the gravity pipe. Velocity = 3m/s. Detention time in the well = 20 min. Use cylindrical well.

## Slide 14
Strainer
Q =Qt /2 =10/2 =5 m3/min
Flow velocity (entrance to the strainer) = 0.15 m/s
A =Q/v =5/(0.15*60) = 0.55 m2 = Effective area
Gross area = 0.55* 2 =1.1 m2
Strainer area =π.d.h
Strainer diameter =1.1/(π*0.6) = 0.6 m
Gravity pipe
v =1.5 m/s
Gross sectional area = Q/v = 5/(1.5*60) = 0.055 m2, Pipe diameter = (4*0.055/π )0.5 = 0.265 m
Washing pipe
Use Q for the washing pipe = 1/3 Q for the gravity pipe.
Q =5/3 =1.67 m3/min
v = 3 m/s
Gross sectional area =1.67/ (3*60) = 0.009 m2, Pipe diameter = (4*0.009/π )0.5 = 0.11 m
Size of the well
Detention time = 20 min
Effective volume =Q *time = 5*20 =100 m3
Effective well depth = 252 - 249 + (1-0.6) = 3.4 m
Cylindrical well
Effective volume = area* effective depth
Area (sectional area) =100/3.4 = 29.4 m2
Well diameter = (4*29.4/π )0.5 = 6.1 m