## Slide 1: Aggregate
Doha M. Abdul-Razzaq Al Saffar
Al Mansour University College
Civil Engineering Department
2017

## Slide 2: General
Aggregate was originally viewed as on inter material dispersed throughout the cement paste largely for economic reasons ¸ at last three quarters of the volume of concrete is occupied by aggregate.
Aggregate is cheaper than cement and it is ¸there for¸ economical to put into mix. But economy is not only reason for using aggregate it confers considerable technical advantages on concrete which has a higher volume stability and better durability than hydrated cement paste alone

## Slide 3: Classification
A. Fine aggregate:
It is the aggregate most of which passes (95-100) ¸ through a 4.75 mm sieve and contains only so much coarser material as is permitted by specification . Sand considered having lower size limit of about 0.07mm.
The fine aggregate may be one of the following
1. Natural Sand: is resulting from disintegration of rock
2. Crushed stone sand: produced by crushing natural hard stone.
3. Crushed gravel sand: the fine aggregate produced by crushing natural gravel
4. Silt particle size material between 0.06mm-0.002mm.
5. Clay particle size material smaller than 0.002mm.

## Slide 4: Classification
B. Coarse aggregate:
The aggregate most of which retained on the 4.75mm sieves the coarse aggregate may be one of the following:
1. Uncrushed gravel: resulting from natural disintegration of rock
2. Crushed gravel: obtained by the crushing gravel or hard stone
3. Partially crushed stone obtained as product of blending of the above two types
C. All_ in_ aggregate:
Sometimes combined aggregate are available in nature comprise different fractions of fine and coarse aggregate.