## Slide 1: Aggregate
Doha M. Abdul-Razzaq Al Saffar
Al Mansour University College
Civil Engineering Department
2017

## Slide 2: Properties of Aggregate
shape of aggregate :
a. Roundness : its measure the relative sharpness or angular of the edges and corner of particle .
Roundness depend on strength and a bras on resistance . of the parent rock.
. The amount of wear to which the particle has been subjected
In the case of crushed aggregate ,the particle shape depends on - nature of the parent material.
- Types of crusher.
- Reduction ratio (the ratio of the size of material fed into crushed , the size of finished product )
The angularity of aggregate can be estimated from the proportion of voids in sample compacted in a prescribed way.

## Slide 3: b. Sphencity :
Its defined as a function of the ratio of the surface area of the particale to its volume .
Partials with a high ratio of surface area to volume of particular interest as they increase the water demand for given workability of the concrete mix.
Two types of particles which depart from equidimensional shape are interest
elongated
Flaky
It can also affect adversely the durability of concrete because flaky particles tend to be obtained in one plane with bleeding water and air voids forming underneath.

## Slide 4: Bond between aggregate and Cement Paste
Is an important factor in the strength of cone rate it is depend on :
1. interlocking of aggregate and hydrated Cement Paste: due to (the roughness of the surface of the former, such as that of crushed particles , results in better bond due to mechanically interlocking
2. physical and chemical properties of aggregate :
Related to its mineralogical and chemical composition. For instance, some chemical bond may exist in the case of limestone, dolomite .
3. Strength of the hydrated Cement Paste :
Bond strength increases with the age of concrete , it seem that the ratio of bond strength to the strength of hydrated Cement Paste increase with age .

## Slide 5: Surface texture :
Surface texture of the aggregate affects its bond to the cement paste and also influences the water demand of the mix, especially in the case of fine aggregate.
The majority of natural aggregates have specific gravity of between 2.6 and 2.7.

## Slide 6: Bulk Density:
The bulk density of aggregate is defined as the mass of the material in given volume and it expressed kg\m3
The bulk density clearly depends on how densty the aggregate is packed , the size distribution, and shape of particles .
For coarse aggregate of given specific gravity, a higher bulk density means that there are fewer voids to be filled by fine aggregate and cement.

## Slide 7: Porosity and Absorption of Aggregate:
The porosity of aggregate, its permeability, and absorption influence:
- bond between the aggregate and cement paste
- The resistance of concrete to freezing and thawing.
- Chemical stability.
- Resistance.
The pores in aggregate vary in size over wide range:
The largest being large enough to be seen under micro-scope or even with the naked eye.
But even the smallest aggregate pores are larger than the gel pores in the cement paste.