## Slide 1: Aggregate
Doha M. Abdul-Razzaq Al Saffar
Al Mansour University College
Civil Engineering Department
2017

## Slide 2: PARTICLE SHAPE & SURFACE TEXTURE
In addition to petrological character, the external characteristics, i.e. The shape & surface texture of aggregates are of importance.
Particle Shape
Rounded: Completely water worn & fully shaped by attrition. (River Gravel)
Irregular: Partly shaped by attrition so it contains some rounded edges. (Land Gravel)

## Slide 3
Angular: Has sharp corners, show little evidence of wear. (Crushed Stone)
Flaky: Thickness is relatively small with respect to two other dimensions. (Laminated Rocks)
Elongated: Have lengths considerably larger than two other dimensions.

## Slide 5
Rounded aggregates are suitable to use in concrete because flaky & elongated particles reduce workability, increase water demand & reduce strength.
In the case of angular particles, the bond between agg. Particles is higher due to interlocking but due to higher surface area, angular particles increase water demand & therefore reduce workability. As a result, for the same cement content & same workability rounded agg. Give higher strength.

## Slide 6: Surface Texture
This affects the bond to the cement paste & also influences the water demand of the mix.
1. Smooth: Bond b/w cement paste & agg is weak.
2. Rough: Bond b/w cement paste & agg. is strong.
Surface texture is not a very important property from compressive strength point of view but agg. Having rough surface texture perform better under flexural & tensile stresses.

## Slide 7
.