## Slide 1
Resultant of Non-Concurrent Forces
In the case of a coplanar force system, the lines of action of all the forces lie in the same plane, Fig. a, and so the resultant force FR = ΣF of this system also lies in this plane. Furthermore, the moment of each of the forces about any point O is directed perpendicular to this plane. Thus, the resultant moment (MR)O and resultant force FR will be mutually perpendicular, Fig. b. The resultant moment can be replaced by moving the resultant force FR a perpendicular or moment arm distance d away from point O such that produces the same moment (MR)O about point O, Fig. c. This distance d can be determined from the scalar equation (MR)O = FR.d = ΣMO or d = (MR)O / FR
Lecture 5

## Slide 2
Example : Replace the force and couple moment system acting on the beam in Fig. a by an equivalent resultant force, and find where its line of action intersects the beam, measured from point O.
Solution:
From Fig. b, the magnitude of FR is