## Slide 1
Resultant of Parallel Force System.
The parallel force system shown in Fig. a consists of forces that are all parallel to the z axis. Thus, the resultant force FR = ΣF at point O must also be parallel to this axis, Fig. b. The moment produced by each force lies in the plane of the plate, and so the resultant couple moment, (MR)O will also lie in this plane, along the moment axis a since FR and (MR)O are mutually perpendicular. As a result, the force system can be further reduced to an equivalent single resultant force FR , acting through point P located on the perpendicular b axis, Fig. c. The distance d along this axis from point O requires (MR)O = FR.d = ΣMO or d = (MR)O / FR
Lecture 6

## Slide 2
Example : The slab in Fig. a is subjected to four parallel forces. Determine the magnitude and direction of a resultant force equivalent to the given force system and locate its point of application on the slab.