## Slide 1
Static Equilibrium of a Particle
A particle is said to be in equilibrium if it remains at rest if originally at rest, or has a constant velocity if originally in motion. To maintain equilibrium, it is necessary to satisfy
Newton’s first law of motion, which requires the resultant force acting on a particle to be equal to zero.
The Free-Body Diagram
A drawing that shows the particle with all the known and unknown the forces that act on it is called a free-body diagram (FBD). To construct a freebody diagram, the following three steps are necessary.
Draw Outlined Shape.
Imagine the particle to be isolated or cut “free” from its surroundings by drawing its outlined shape.
Show All Forces.
Indicate on this sketch all the forces that act on the particle. These forces can be active forces, which tend to set the particle in motion, or they can be reactive forces which are the result of the constraints or supports that tend to prevent motion. To account for all these
forces, it may be helpful to trace around the particle’s boundary, carefully noting each force acting on it.
Identify Each Force.
The forces that are known should be labeled with their proper magnitudes and directions. Letters are used to represent the magnitudes and directions of forces that are unknown.
Lecture 7

## Slide 2
Cables and Pulleys.
A cable can support only a tension or “pulling” force, and this force always acts in the direction of the cable. the tension force developed in a continuous cable which passes over a frictionless pulley must have a constant magnitude to keep the cable in equilibrium. Hence, for any angle θ shown in Fig. below, the cable is subjected to a constant tension T throughout its length.
Note : All cables (or cords) will be assumed to have negligible weight and they cannot stretch.
Springs. If a linearly elastic spring (or cord) of undeformed length lo is used to support a particle, the length of the spring will change in direct proportion to the force F acting on it.
F=k.s
Where k is the spring constant or stiffness and s = l-lo

## Slide 3
EXAMPLE : Determine the tension in cables BA and BC necessary to support the 60-kg cylinder in Fig. a.