## Slide 1: Lecture 1
Estimation and Costing
Asst. Lect. Ali Khalid

## Slide 2: Estimation and Costing
Introduction:
Estimating is the technique of calculating or Computing the various quantities and the expected Expenditure to be incurred on a particular work or project.
In case the funds available are less than the estimated cost the work is done in part or by reducing it or specifications are altered, the following requirement are necessary for preparing an estimate.
1. Drawings like plan, elevation and sections of important points.
2. Detailed specifications about (Architectural, structural and MEP drawings) & properties of materials etc.
3. Standard schedule of rates of the current year.

## Slide 3: Introduction
NEED FOR ESTIMATION AND COSTING
1. Estimate give an idea of the cost of the work and hence its feasibility can be determined whether the project could be taken up with in the funds available or not.
2. Estimate gives an idea of time required for the completion of the work.
3. Estimate is required to invite the tenders and Quotations and to arrange contract.
4. Estimate is also required to control the expenditure during the execution of work.
5. Estimate decides whether the proposed plan matches the funds available or not.

## Slide 4: Introduction
There are several kinds of estimating techniques; these can be grouped into two main categories: 1. Approximate Estimations. 2. Detailed Estimations.
1. Approximate Estimations: this type of estimation is useful before starting detailed design.
The main objectives of this type of estimation are:
1. To estimate the cost of construction approximately in a short time.
2. To carry out a comparative study between different design alternatives.
3. To get an estimate of construction that will be compared later with the more detailed estimation after completion the design

## Slide 5: Introduction
Types of Approximate Estimations:
Floor Area Method: in this method an approximate cost (material and labour) per square meter will be used for this estimation. This cost per square is either used evenly among all stories or may be higher relatively for lower stories
Cubical Method: This method is more accurate than the square meter of floor area method. Since it takes into account the third dimension (the height)

## Slide 6: Introduction
2. Detailed Estimations:
Detailed estimate of the cost of a project is prepared by determining the quantities and costs of everything that a contractor is required to provide and do for the satisfactory completion of the work.
Steps in Preparation of an Estimate
1. Taking off Dimension:
2. Squaring Dimension:
3. Working up Abstraction
4. Billing of quantities:

## Slide 7: Introduction
Measurement of Materials and Works:
The units of measurements are mainly categorized for their nature, shape and size and for making payments to the contractor. The principle of units of measurements normally consists of the following:
1. Single units work like doors, windows, trusses etc., are expressed in numbers.
2. Works consists linear measurements (L.M) involve length like pipe.
3. Works consists of a real surface measurements involve area like plastering, white washing, partitions of specified thickness etc., are expressed in square meters (m2).
4. Works consists of cubical contents which involve volume like earth work, cement concrete, Masonry etc. are expressed in Cubic meters