## Slide 1: Lecture 10
Tractors
Asst. Lect. Ali Khalid

## Slide 2
Are self-contained units that are designed to provide tractive power for drawbar work, because they are low center of gravity machines.
Tractors are classified on the basis of running gear to:
Crawler Track.
Wheel Track.

## Slide 3
 | Wheel Tractor |  | Crawler Tractor
1 | Good on firm soils and concrete. | 1 | Can work on a variety of soils.
2 | Best for level and downhill work. | 2 | Can work over almost any terrain.
3 | Wet weather, causing soft and slick surfaces conditions, will stop operation. | 3 | Can work on soft ground, and over mud- slick surface.
4 | Good for long travel distance. | 4 | Good for short work distance.
5 | Fast return speeds 8-20 mph | 5 | Slow return speed 5-7 mph

## Slide 4
Selecting of tractor:-
In selecting tractor several factors should be considered:
The size required for a given job.
The kind of job for which it will be used.
Bulldozing.
Pulling a scraper.
Ripping.
Clearing land, etc.
The type of ground over which it will operate.
The firmness of the haul road.
The smoothness of the haul road.
The slope of the haul road.
The length of haul road.
The type of work it will do after this job is completed.

## Slide 5
Procedure for reading a performance charts:
Ensure that the proposed machine to be utilized has the same engine, gear ratios, and tire size.
Determine the machine weight.
Estimate a total resistance
Rolling resistance (%) =
plus grade resistance (%)) based on the probable job conditions.
-The intersection of the vehicle weight line and the total resistance line established the conditions under which the machine will be operated and the power requirement.
-Extend a line horizontally from the weight total resistance intersection point from these point at which the horizontal line interests the gear range curve, drop a line vertically to the speed axis. This yield the vehicle speed for the assumed job conditions.

## Slide 6
Bulldozer
Is a tractor unit that has a blade attached to the machine front. It is designed to provide attractive power for drawbar work. The amount of material the dozer moves is dependent on the quantity that will remain in front of the blade during the push.
Bulldozers are used in:
It is used in moving earth or rock for short hand (push) distance up to 300 ft. (91 m) in the case of large dozers.
Spreading earth or rock fills.
It is used in backfilling trenches.
It is used in opening up pilot roads through mountains or rocky terrain.
Clearing the floors of borrow and quarry pits.
Helping load tractor –pulled scrapers.
It is used in clearing land of timber, stumps, and root mat.

## Slide 7
Straight (S) blade: is designed for short and medium distance passes, such as backfilling, grading and spreading fill material.
2.Angle blades (A): is wider (face length) by 1to 2 ft. than (S) blade. It can be angle up to a maximum of 25 degrees left or right to the dozer line of travel used for side casting material, backfilling or making side hill cuts.
3-Universal blade (U): Its blade is wider than a straight blade and having a 25ᵒ wings to reduce the loose soil spillage.
4- Semi – U (SU) blade: It is similar to the U type but with shorter wings.
5- Cushion (C) blade: Its blade is shorter than a straight blade. It is usually mounted on large dozers that are used to push-loading scrapers.

## Slide 9
Bulldozer Production estimating:
The amount of material that the dozer moves depends on the quantity which will remain in front of the blade during the push. The production depends on:
The blade type.
The type and condition of material.
The cycle time.
The load that a blade will carry can be estimated by several methods:-
The manufacture blade ratings.
The previous experience (similar material equipment, and work conditions).
The field measurements.
The manufactures usually provide a blade rating that is based on:
Vs = 0.8 LH2

## Slide 10
Example:
A (D7G) crawler tractor with a straight blade is to be used in dozing operation to a site with dimensions () m .find the minimum time in hours needed to excavate this site with a depth of 30 cm with the below information:-
Blade dimension type S () m
Operation factor 50 min / hr Swell % = 25 %
Push speed 2.4 km/ hr
Return speed 5.6 km / hr Fixed time = 0.32
Solution:
= = Loose measure.
Cycle time =
Out put =
Min. time = volume/output(100*50*0.3) / 22.35 = 67 hr
Cycle time = +
Trip / hr = 50/ 2.105 = 23 . 75
Out put =
Min. time =