## Slide 1: Lecture 11
Scrapers
Asst. Lect. Ali Khalid

## Slide 2
Scrapers
Introduction:
The scraper is an equipment which is used to excavate, load, haul, and dump soil over a medium to long hauling distances. It excavates or cuts the soil by lowering the front edge of its bowl into soil.
A typical type of such equipment is shown in Fig.(1) below.

## Slide 3
Scraper Types:
The main types of scrapers are:
Pusher-Loaded scrapers.
Self-loading scrapers.
For easy to load soil (i.e not for a rocky ground), a self-loading scraper may be used up to a haul distance of about 250m. For longer haul distances a pusher-loaded scraper is required to assist in using the scraper for loading and transporting of soil.

## Slide 4
Pusher-loaded scraper:
-Single-powered axle
-Tandem-powered axles: The heavier scraper types have two engines (‘tandem powered’), one driving the front wheels, one driving the rear wheels.

## Slide 5
Self-Loading Scrapers:
The main types of these scrapers are:
Type(1):. Elevating wheel-tractor scraper:
In which a chain elevator is mounted on the front of the bowl to increase the amount of the collected soil in the bowl. It is economical to be used in short hauling distances.

## Slide 6
For the haul conditions as stated below, analyze probable scraper production if the total length of haul when moving from the cut to the fill is 4000 ft as follows:-
Soil density = 3100 lb / bank cy
Average load time of 0.85 min and the expected load from load growth curve will be 96% of capacity.
Swelling 25%
Capacity of scraper( heaped) = 31 cu-yd
Weight of scraper empty = 96880 lb
Fixed time equal to 0.45 min.