## Slide 1: Lecture 12
Excavating Equipment
Asst. Lect. Ali Khalid

## Slide 2
There are many types of equipment which are used to excavate earth and rock in construction operations include the following machines:-
Front shovels.
Hoes.
Dragline.
Clamshells.

## Slide 3
Front Shovels:
Front shovels are used for:
Digging and loading earth or fragmented rock and for mineral extraction.
Limited ability to dig below track level.
Efficient when digging above track level

## Slide 4
Factors affect Productivity:
Class of material.
Height of Cut.
Angle of swing.
Operator skill.
Condition of the shovel.
Size of hauling units.
Handling of oversize materials.
Cleanup of location area.

## Slide 5
Draglines:
Dragline excavations especially useful when there are need for extended reach in excavating or when material must be excavated from under water.

## Slide 6
The greatest advantage of a dragline over other machines is its long reach for digging and dumping.
Dragline is designed to excavate below the level of the machine.
Dragline is used to excavate and load material into hauling units, such as trucks.

## Slide 7
Clamshells: are commonly used for excavating vertical shafts and footings, unloading bulk materials from rail cars and ships, and moving bulk material from stockpiles to bins, hoppers, or haul units.
Front end loaders: - are used in the construction work (earth and rock):
It is used to:
Load trucks.
Excavate earth as bulldozers.
Handle and transporting heavy items such as parts of equipment

## Slide 8
Example :-
Find the number of trucks worked with front end loader with no lost time waiting for trucks with the following information:-
Truck :
Capacity of truck = 10 m3 Loose measure.
Loading speed = 60 Km / hour Fixed time = 5 min
Empty speed = 80 km / hour Operating factor = 50 min/hr.
Haul distance = 48 km
Front end loader:-
Haul distance = 50 m Loading speed = 78 m / min
Operating factor = 45 min/hr. Empty speed = 97 m / min
Swelling percentage = 25% heaped Capacity = 4 m3 loose measure
Solution:
No. of trucks =
Productivity of front end / hr =
= 0.9
Productivity of truck / hr =
No. of trucks = =20 trucks