## Slide 1: Lecture 2
Detailed Estimations
Asst. Lect. Ali Khalid

## Slide 2: Detailed Estimations
Methods of Measurements:
Group System Method:
In this method, the project is divided into different work groups. For convential buildings for instance, the work groups are:
Work items below N.G.L. (i.e., foundations).
Reinforced concrete skeleton work (columns, beams and slaps).
Partitioning.
External and internal plastering.
Tiling.
Mechanical works (air conditioning).
Electrical works.
Plumbing.
Item no. | Description of items | Dimensions | Quantity | Notes

## Slide 3: Detailed Estimations
2. Trade System Method (Local Method):
In this method the project is divided into different activities. The activities are arranged into sequential order. It is the most common and popular method. Below is the typical table used in this method
Sq | Item (description) | Unit | Number | Dimensions |  |  | Quantity |  | Final Quantity
 |  |  |  | Length | Width | Height | + | - | 
1 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
3 |  |  |  |  |  |  |  |  | 

## Slide 4: Detailed Estimations
Length Measurements:
There are two methods for length measurements which are:
1. Axis Method: in this method, the plan is divided into groups of equal lengths.
Example (1): The strip footing plan shown below is divided into two length groups:
Solution:
Group one: consist of three parts, each of length (A)
Group two: consist of four parts, each of length (B)

## Slide 5: Detailed Estimations
2. Central Lines Method: this is the more common and popular method
Example (1):
Use the central lines method, calculate the total length of the wall footing (strip footing) plan shown below. The footing width is 1.2 meter.

## Slide 6: Detailed Estimations
Application examples
Example (1):
Estimate the quantities of the construction items below the D.P.C for the plan shown in fig. use the group system method and the central lines method for this plan.

## Slide 7: Detailed Estimations
Item no. | Description of items | Dimensions | Quantity | Notes
1. | Earth Excavations |  |  | 
2. | Hard core |  |  | Use point 0.8m brick as a hardcore
3. | Concrete (plain) |  |  | Concrete ( 1:2:4) by volume, c = 25 Mpa
4. | Brick wall |  |  | Brick work using cement mortar ( 1:3) by volume
 | 0.48m width |  |  | 
 | 0.36m width |  |  | 
 | 0.24m width |  |  | 
5 | D.P.C. |  |  | Use 0.15m D.P.C
Item no. | Description of items | Dimensions | Quantity | Notes
1. | Earth Excavations |  |  | 
2. | Hard core |  |  | Use point 0.8m brick as a hardcore
3. | Concrete (plain) |  |  | 
4. | Brick wall |  |  | Brick work using cement mortar ( 1:3) by volume
 | 0.48m width |  |  | 
 | 0.36m width |  |  | 
 | 0.24m width |  |  | 
5 | D.P.C. |  |  | Use 0.15m D.P.C