## Slide 1: Soil Formation

## Slide 2
Depending on the method of deposition, soils can be grouped into two categories:
Residual soils: The soils which remain at the place of disintegration of parent rock.
Transported soils: The soils, which carried away from their place of disintegration to some other place by transporting agencies. The transporting agencies may be classified as: i) water ii) wind iii)gravity iv) Ice
Soil
Is any un-cemented or weakly cemented accumulation of mineral particles formed by weathering of rocks, the void between the particles containing water/ or air.

## Slide 3
1- Mechanical (Physical weathering):
All type of actions that cause a disintegration of the parent rocks by physical means such as, gravity, wind and water. The product of this type is rounded, sub rounded or granular, its products called coarse grained soil e.g. (gravel and sand ) they present in nature in a single grain structure . It properties are the same as parent rock.
Coarse grained soil
Sand & Gravel
Cohesion less soil
2- Chemical weathering
All types of chemical reactions that occur between the minerals of the rock and the environment (air, water ---et.) and will end up by disintegration of parent rock into fine grain particles; these products have different properties from the parent rock. They present in nature as a lumps of number of plate like particles. The physical property of this product does not reflect the same properties of the parent rocks.
Fine grained soil
Silt and clay
Cohesive material
Weathering Which are usually results from atmospheric processes action on the rock at or near the earth surface.

## Slide 4
Tetrahedral Unit :
Consists of four oxygen atoms (or hydroxyls, if needed to balance the structure) and one silicon a tom.
Octahedral Unit:
Consist of six hydroxyl ion at apices of an octahedral enclosing an aluminum ion at the center.
Clay minerals: There are two basic structure units that form types of the minerals in the clay:

## Slide 5
Kaolinite:
The most common mineral is kaolinite. The structure is composed of a single tetrahedral sheet and a single alumina octahedral sheet. Strong Hydrogen Bond So not affected by water. And its also called China clay
Formation of Minerals
The combination of two sheets of silica and gibbsite in different arrangements and condition lead to the formation of different clay minerals such as

## Slide 6
Illite has a basic structure consisting of two silica sheets with a central alumina sheet. There is a potassium bond between the layers. Slightly affected by water
Montmorillonite unit: The basic structural unit is similar to that of Illite. Highly affected by water with high shrinkage and Swell and it is called expansive soil.

## Slide 7
Clay Particle –water relations:
The negative charge on the surface of the soil particle therefore attracts the positive (hydrogen) end of the water molecules. More than one layer of water molecules sticks on surface with considerable force decrease with increase in the distance of the water molecule from the surface.
The electrically attracted water surrounds the clay particle is known as the diffused double-layer of water. The water located within the zone of influence is known as the adsorbed layer.

## Slide 8
If there is net repulsion the particles tend to assume a face-to-face orientation, this being referred to as a dispersed structure.
If there is net attraction the orientation of the particles tends to be edge-to-face or edge-to-edge, this being referred to as a flocculated structure.
Clay Structures

## Slide 9
Assemblages can also occur in the form of connectors or a matrix between larger particles. An example of the structure of a natural clay, in diagrammatical form, is shown in Figure (e).
In natural clays, which normally contain a significant proportion of larger, bulky particles, the structural arrangement can be extremely complex. Two possible forms of particle assemblage, known as the bookhouse and turbostratic structures, are illustrated in Figures .