## Slide 1: Plasticity of Fine Grained Soils

## Slide 2
Plasticity is the ability of a soil to undergo unrecoverable deformation at constant volume without cracking or crumbling. It is due to the presence of clay minerals or organic material.
Consistency limits (Atterberg limits):
Atterberg, a Swedish scientist developed a method for describing the limit consistency of fine grained soils on the basis of moisture content. These limits are liquid limit, plastic limit and shrinkage limit.

## Slide 3
Liquid limit (L.L): is defined as the moisture content in percent at which the soil changes from liquid to plastic state.
Plastic Limit (P.L.): The moisture contents in % at which the soil changes from plastic to semi solid state.
Shrinkage Limit (S.L.): The moisture contents in % at which the soil changes from semi solid to solid state.
Plasticity Index (P.I.): it is the range in moisture content when the soil exhibited its plastic behavior: