## Slide 1: Soil Compaction

## Slide 2
Soil compaction is one of the most critical components in the construction of roads, airfield, embankments and foundations. The durability and stability of a structure are related to the achievement of proper soil compaction. Structural failure of roads, airfield and the damage caused by foundation settlement can often be traced back to the failure to achieve proper soil compaction.

## Slide 3
Compaction of soil:
Compaction is the process of increasing the density of a soil by packing the particles closer together with a reduction in the volume of air only. Compaction increases the dry density and decreases the void ratio.
Purpose of compaction:
1- Increase shear strength of soil
2- Reduce void ratio thus reduce permeability
3- Controlling the swell-shrinkage movement
4- Reduce settlement under working load
5- Prevent the buildup of large water pressure

## Slide 14
Measurement of field Density
1- Core cutter
5- Radiation Technique.
2- Sand Replacement method.
3- Rubber Balloon method .
4- Penetrating Needle