## Slide 1: Soil Permeability and Flow Examples

## Slide 3
There are three heads which must be considered in problem involving fluid flow in soil:
1- Pressure head (ℎp) : is the pizometer reading = pore water pressure /unit weight of water
2- Elevation head at any point (ℎe): is the vertical distance above or below some reference elevation or datum plane.
3- Total head, ℎ= ℎp+ℎe

## Slide 4
Example 1: For the Setup shown, plot: ht, he, hp and the velocity of flow?

## Slide 5
Example 2
For the setup shown, Draw, ht, he , hp and velocity of flow ?

## Slide 6
Example 3 For the setup shown
A) Calculate the pressure head, elevation head, total head and head loss at points B, C,D and F in centimeter of water. b)-Plot the heads versus the elevation

## Slide 8
Example 4:For Setup shown: Soil I , A= 0.37 m2 , n=0.5 and k= 1 cm/sec, Soil II, A= 0.186 m2 , n=0.5 and k=0.5 cm/sec.