## Slide 1
College : Mansour University
Department : Computer Science and information System
Prepared by
Dr. Adil Abbas Majeed
2018-2019
Architecture
Digital Logic Circuit
Chapter One

## Slide 2
Digital Computer
Combinational Circuit
Sequential Circuit
Decoder
Multiplexer
Registers
Microoperations
Outline

## Slide 3
1. Digital Computers
  1. Digital Computers
The digital computer is a digital system that performs various computational tasks. The word “digital” implies that the information in the computer is represented by variables that take a limited number of discrete values.
Digital Computers use binary number system, which has two digits: 0 and 1. A binary digit is called bit.
  2. Computer System
It is subdivided into two functional entities: hardware and software. The hardware of the computer consists of all the electronic components and electromechanical device. The hardware of the computer is divided into three parts (Central Processing Units “CPU”, Memory and I/O units).
a. CPU: It is consists of two sections (data section or processor unit that contains the Arithmetic Logic Unit “ALU” and number of registers) and the control section which interpret instructions and effects register transfer.

## Slide 4
b. Memory unit: It is used to store the instructions and data.
c. Input / Output Units: It is consists of input and output devices and the input and output processors (IOP) for controlling the transfer of information between the computer and the outside world.
Computer software consists of the instructions and data that the computers manipulate to perform various data processing tasks.
Memory Unit
Central Processing Unit (CPU)
Internal Bus
Processor Unit
Control Unit
ALU
Registers
Input-Output Processor (IOP)
Output Device
Input Device
External Bus
External Bus
Figure: Digital Computer block diagram.

## Slide 5
2. Combinational Circuit
Combinational
Circuit
It is connected arrangement of logic gates with a set of input and outputs. The n binary input variables come from an external source, the m binary output variables go to an external destination, and in between there is an interconnection of logic gates. It is transform binary information from the given input data to the required output data.
It is described by a truth table showing binary relationship between the n input variables and the m output variables. Combinational circuits in which there are no feedback paths from output to input and there is no memory.
n Input Variables
m Output Variables
Figure 2: Block diagram of Combinational Circuit.

## Slide 6
3. Sequential Circuit
It is an interconnection of flip-flops and gates. The gates by themselves constitute a combinational circuit, but when included with the flip-flops, the overall circuit is classified as sequential circuit. Sequential circuits in which feedback paths exist from outputs to input and they have memory.
Combinational Circuit
Flip-Flop
Clock
Inputs
Outputs
Figure 3: Block diagram of a clocked synchronous sequential circuit.
Sequential circuit | Combinational circuit
uses flip flops | connected arrangement of logic gates
feedback paths exist from outputs to input | there are no feedback paths from output to input
compute their output based on input and state | implement Boolean functions, so they are functions only of their inputs
the state is updated based on a clock | not based on clocks
They Have memory | There is No memory
Q: What is the difference between the combinational and sequential circuit?

## Slide 7
4. Decoder
E | Input | D3 | D2 | D1 | D0
0 | × × | 0 | 0 | 0 | 0
1 | 0 0 | 0 | 0 | 0 | 1
1 | 0 1 | 0 | 0 | 1 | 0
1 | 1 0 | 0 | 1 | 0 | 0
1 | 1 1 | 1 | 0 | 0 | 0
It is combinational circuit that converts binary information from the n coded inputs to a maximum of 2n unique output. It is implemented with AND gates, in some times with NAND gates.
The decoders presented are called n to m line decoders presented are called n to m line decoder.
Example: What the truth table and draw circuit for 2 × 4 line decoder.
Truth Table for 2 × 4 line decoder.

## Slide 8
Example 1: Implement a Full Adder with decoder and two OR gates
S (x, y, z) = 1, 2, 4, 7
C(x, y, z) = 3, 5, 6, 7
Sol:
Example 2: Implement a Full Adder with decoder and two OR gates
Sol:
 | Input |  |  | Output | 
 | X | Y | Z | F1 | F2
0 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1 | 1
2 | 0 | 1 | 0 | 0 | 1
3 | 0 | 1 | 1 | 0 | 1
4 | 1 | 0 | 0 | 0 | 0
5 | 1 | 0 | 1 | 0 | 0
6 | 1 | 1 | 0 | 1 | 1
7 | 1 | 1 | 1 | 0 | 1

## Slide 9
5. Multiplexer
It is combinational circuit that receives binary information from one of 2n input data lines and directs it to a single output line.
The selection of a particular input data line for the output is determined by a set of selection inputs.
Select S1 S0 | Output Y
0 0 | I0
0 1 | I1
1 0 | I2
1 1 | I3
Figure: 4×1 line multiplexer Truth Table

## Slide 10
6. Registers
It is a group of flip-flops with each flip-flop capable of storing one bit of information. An n bit register has a group of n flip-flop and is capable of storing any binary information of n-bits.
A register consists of a group of F-Fs and gates that effect their transition. The F-Fs hold the binary information and the gates control when and how new information is transferred into the register.
Figure: 4-Bit Register

## Slide 11
Bus and Memory Transfer
A more efficient scheme for transferring information between registers in a multiple-register configuration is a common bus system.
A Common bus system is bus structure consists of a set of common lines, one for each bit of a register, through which binary information is transferred one at a time.
Figure: Common Bus System for four Register.

## Slide 12
A microoperation is an elementary operation performed on the data stored in register example: load, clear, and shift. The types of microoperations in digital computers are classified into four categories:-
Register transfer microoperation.
Arithmetic microoperation.
Logic microoperation.
Shift microoperation.
7. Microoperations
1. Register Transfer Microoperation
Computer registers are designated by capital letters (sometimes followed by numerals) to denote the function of the register.
Ex. 1: Design circuit to transfer data from register (R1) to another register (R2) under condition: If (P = 1) then (R2 = R1)
Sol.:
P : R2 R1
P is Boolean variable (0 or 1).

## Slide 13
2. Arithmetic microoperation and Circuit
The basic arithmetic microoperations are addition, subtraction, increment and decrement. The arithmetic microoperation is specified as “add”.
R3 R1 + R2
The other arithmetic microoperations are listed in table below:-
Microoperation | Description
R3 R1 + R2 | Addition
R3 R1 - R2 | Subtraction
R3 | 1’s complement
R3 +1 | 2’s complement
R3 R1 + +1 | Subtraction using 2’s complement
R1 R1 + 1 | Increment
R1 R1 - 1 | decrement
Microoperation | Description
R3 R1 + R2 | Addition
R3 R1 - R2 | Subtraction
 | 1’s complement
 | 2’s complement
 | Subtraction using 2’s complement
R1 R1 + 1 | Increment
R1 R1 - 1 | decrement
Combinational
Circuit
X n-input
Parallel Adder
Y
n F = A + Y + Cin
Figure: Block diagram of an arithmetic circuit.
n
n
A
B
S0
S1

## Slide 14
Select | Input | Output | Microoperation
S1 S0 Cin |  |  | 
0 0 0 | A B | F = A + B | Add
0 0 1 | A B | F = A + B + 1 | Add with carry
0 1 0 | A | F = A + | Subtract with borrow
0 1 1 | A | F = A + +1 | Subtract
1 0 0 | A 0 | F = A | Transfer
1 0 1 | A 0 | F = A + 1 | Increment
1 1 0 | A 1 | F = A - 1 | Decrement
1 1 1 | A 1 | F = A | Transfer
Select | Input | Output | Microoperation
S1 S0 Cin |  |  | 
0 0 0 | A B | F = A + B | Add
0 0 1 | A B | F = A + B + 1 | Add with carry
0 1 0 |  |  | Subtract with borrow
0 1 1 |  |  | Subtract
1 0 0 | A 0 | F = A | Transfer
1 0 1 | A 0 | F = A + 1 | Increment
1 1 0 | A 1 | F = A - 1 | Decrement
1 1 1 | A 1 | F = A | Transfer
The output of the arithmetic circuit is calculated from F = A + Y + Cin

## Slide 15
Boolean Function | Microoperation | Name
F = 0 | F | Clear
F = X | FX | Transfer X
F = XY | FX  Y | AND
F = X | F X  | 
F = Y | F Y | Transfer Y
F = X  Y | F X  Y | Exclusive
F = X + Y | F X  Y | OR
F = | F | NOR
F = | F | Exclusive-NOR
F = | F | Complement Y
F = X + | F X  | 
F = | F | Complement X
F = +Y | F  Y | 
F = | F | NAND
F = 1 | F all 1’s | Set to all 1’s
F = X | F | 
Boolean Function | Microoperation | Name
F = 0 | F | Clear
F = X | FX | Transfer X
F = XY | FX  Y | AND
F = Y | F Y | Transfer Y
F = X  Y | F X  Y | Exclusive
F = X + Y | F X  Y | OR
 |  | NOR
 |  | Exclusive-NOR
 |  | Complement Y
 |  | Complement X
 |  | NAND
F = 1 | F all 1’s | Set to all 1’s
F = X | F | 
3. Logic Microoperation
Logic microoperations are very useful for manipulating individual bits or a portion of a word stored in a register. The logic microoperations listed in the second column of table below represent a relationship between the binary content of two registers A and B.

## Slide 16
4. Shift microoperation
Shift microoperations are used for serial transfer of data. They are also used in conjunction with arithmetic, logic, and other data-processing operations. The contents of a register can be shifted to the left or the right. There are three types of shifts:-
Logical shift (shl, shr):- one that transfer 0 through the serial input.
0 | Rn-1 | Rn-2 |  | R1 | R­0 |  | Rn-1 | Rn-2 |  | R1 | R­0 | 0
Logical Shift Right Logical Shift Left
 | Rn-1 | Rn-2 |  | R1 | R­0 |  | Rn-1 | Rn-2 |  | R1 | R­0 | 
Circular shift (Cil, Cir):- also known as rotate, circulates the bits of the register around the two without loss of information.
Circular Shift Right Circular Shift Left
Arithmetic shift left (ashl, ashr):- shift signal binary number to the left or right. An arithmetic shift left multiplies a signed binary number by 2 and an arithmetic shift-right divides the number by 2.

## Slide 17
S | Cin = 0 | Cin = 1
0 | A | A+1
1 | A+ | A-B
S | Cin = 0 | Cin = 1
0 | A | A+1
1 |  | A-B
S | Cin = 0 | X | Y | Cin = 1 | X | Y
0 | A | A | 0 | A+1 | A | 0
1 | A+ | A |  | A-B | A | 
S | Cin = 0 | X | Y | Cin = 1 | X | Y
0 | A | A | 0 | A+1 | A | 0
1 |  | A |  | A-B | A | 
Q: Design the following 2 bit arithmetic of condition below:
Sol.:
S1 | S0 | Cin = 0 | Cin = 1
0 | 0 | A+B | A+B+1
0 | 1 | A+ | A++1
1 | 0 | A | A+1
1 | 1 | A-1 | A
S1 | S0 | Cin = 0 | Cin = 1
0 | 0 | A+B | A+B+1
0 | 1 |  | 
1 | 0 | A | A+1
1 | 1 | A-1 | A
S1 | S0 | Cin = 0 | X | Y | Cin = 1 | X | Y
0 | 0 | A+B | A | B | A+B+1 | A | B
0 | 1 | A+ | A |  | A++1 | A | 
1 | 0 | A | A | 0 | A+1 | A | 0
1 | 1 | A-1 | A | 1 | A | A | 1
S1 | S0 | Cin = 0 | X | Y | Cin = 1 | X | Y
0 | 0 | A+B | A | B | A+B+1 | A | B
0 | 1 |  | A |  |  | A | 
1 | 0 | A | A | 0 | A+1 | A | 0
1 | 1 | A-1 | A | 1 | A | A | 1
X
B.F.A
Y
4×1
MUX
Q: Design the following 4 bit arithmetic of condition below:
Sol.:
X
B.F.A
Y
4×1
MUX
Cin
B
0
1
A 4
S1 S0 Cout
F
4

## Slide 18
Thank You For All
Adil-2018