## Slide 1
College : Mansour University
Department : Computer Science and information System
Prepared by
Dr. Adil Abbas Majeed
2018-2019
Architecture
Programmed and Instruction Format
Chapter Two

## Slide 2
A program Definition
An Instruction Definition
Instruction Code Formats
Addressing Mode
Outline

## Slide 3
1. A program Definition
A program residing in the memory unit of the computer consists of a sequence of instructions. The program is executed in the computer by going through a cycle for each instruction.
Each instruction cycle consist of the following phases:
Fetch an instruction from memory
Decode the instruction
Read the effective address from memory if the instruction has an indirect address.
Execute the instruction.
In other words the program is a list of instruction or statements for directing the computer to perform a required data-processing task.

## Slide 4
2. An Instruction Definition
The instruction is divided into two parts
Operation code (opcode)
Operands.
The format of any instruction is write in form below
[<identifier>] <operation> <operands> [<comment>]
Note: Identifier, comment is optional.
Operation (opcode): It is part of the instruction that identifier the operation that is to be performed. For example, typical operations are add, subtract and move.
Each opcode is assigned a unique letter combination called a mnemonic.
Mnemonic example: ADD, SUB, MOV,….etc.
Operands: It is represent RAM memory location (specified by an identified, registers, or literal values.
Size field: indicates the size of the operands for the instruction: byte, word or long word.

## Slide 5
3. Instruction Code Formats
The format of the instruction is usually represented in a rectangular box symbolizing the bits of the instruction. The bits of instruction are divided into groups called fields. The most common fields are:-
The operation code field
The Address field
The Mode field
1. The operation code field: which is a group of bits that define various processor operations, such as add, subtract, complement, shift and etc. The number of bits required for the operation code field depends on the total number of computer instruction. The operation code field most consists of at least n-bits for 2n different instruction.
Ex.: A digital computer has 128 instructions, what is the number of bits required for the operation code field?
2n = 128, for opcode

## Slide 6
n-1 m | m-1 k | k-1 0
Mode field | Opcode field | Operand address field
2. The Address field: which are a group of bits that specifies memory address or a process registers. An instruction must specify not only the operation but also the registers or memory words where the data upon it the operation performed which is called “operand” as well as the register or memory field where the result is to be stored. There are divided to four types as shown below:
Three address instruction: specifies three operands each of which can be a process register or a memory word.
Ex: ADD AX, BX, CX (AX  BX + CX)
Two address instruction: which have two operands such as:
Ex: MOV CX, DX (CX  DX)
One address instruction: All operations are performed on a single register or memory contents. Ex: INC AL (AL  AL + 1)
Zero address instruction: these types of instructions does not has any operand:
Ex: CLC (CF  0)
3.The Mode field: which are a group of bits that specifies the way the operand or the effective address of the operand is determined (m-bits required for 2m modes).
The general instruction format is shown in figure below:

## Slide 7
Instruction Format |  |  | 
26 23 | 22 18 | 17 14 | 13 0
Mode | Opcode | Register address | Memory address
Ex: Find number of mode if you have the following instruction ADD B, R1, no. of register = 15, no. of instruction = 20 and memory size = 15K × 27.
Solution:
No. bit of register address field 2X = 15 ; X = 4 bits
No. bit of opcode field 2N = 20 ; N  5 bits
No. bit of address memory 2M = 15 K ; 24 × 210  M = 14 bits
Total bit of instruction = 27 bits
 No. of mode = 27- (4+5+14) = 4 bits

## Slide 8
4. Addressing Mode
n | Opcode
Memory | 
The addressing mode specifies a rule for interpreting or modifying the address field of the instruction before the operand is actually referenced. There are different types of addressing modes as shown below:
1. Implied Mode: In this mode the operands are specified implicitly in the definition of the instruction (no address field is required).
Ex: CLA, CMA, INC, HLT, CLC, STI and LAHF
n | Opcode | Operand
Memory |  | 
2. Immediate Mode: In this mode the operands are specified in the instruction itself. The operand field contains the actual operand to be used in conjunction with the operation specified in the instruction. Immediate mode instructions are useful for initializing registers to a constant value.
Ex 1: MVI Al, 30
Ex 2: MOV AX,50F0

## Slide 9
Processor Register |  | M | Opcode | Register Address
 |  |  |  | Memory
Operand |  |  |  | 
3. Register Mode: In this mode the operands are in registers that reside within the CPU.
Processor Register |  | M | Opcode | Register Address
Effective Address |  |  |  | 
 |  |  |  | Operand
4. Register Indirect Mode: In this mode the instruction specifies a register in the CPU whose contents give the address of the operand in memory. The advantage of a register indirect mode instruction is that the address field of the instruction uses fewer bits to select a register than would have been required to specify a memory address directly.
Ex 1: MOV A, M
Ex 2: ADD AL, [DI]

## Slide 10
M | Opcode | Effective Address
 |  | Operand
5. Direct Address Mode: In this mode the effective address is equal to the address part of the instruction. The operand resides in memory and its address is given directly by the address field of the instruction.
Ex. 1: LDA 2000
Ex. 2: MOV SI, [2040]
M | Opcode | Memory Address
 |  | Effective Address
 |  | Operand
6. Indirect Address Mode: In this mode the address field of the instruction gives the address where the effective address is stored in memory.

## Slide 11
M | Opcode | Address
 |  | Next instruction
Program Counter (PC) + Address |  | 
 |  | Operand
7. Relative Address Mode: In this mode the content of the program counter is added to the address part of the instruction in order to obtain the effective address.
Effective address = Address Part + PC
Index Register |  | M | Opcode | Address
 |  |  |  | 
 |  |  |  | Operand
8. Indexed Address Mode: In this mode the content of an index register is added to the address part of the instruction to obtain the effective address. The index register is a special CPU register that contains an index value.
Ex: MOV AL, 40D0[XR]

## Slide 12
20 | 10
30 | 90
60 | AND A, address
61 | 30
62 | Next instruction
80 | 45
90 | 20
92 | 30
100 | 80
Address Mode | Accumulator | Effective Address
Immediate | 38 & 30 = 30 | 61
Direct | 38 & 20 = 20 | [30] = 90
Indirect | 38 & 10 = 10 | [30]= [90]= 20
Relative | 38 & 30 = 30 | 62+30 = 92
Ex 1: A two word AND instruction stored at location 60 in memory with its address part at location 61 contain the value 30, as shown in figure below. Find the effective address and the accumulator value for the following address.
(Hint: All Values in Hexadecimal)
Immediate.
Direct.
Indirect.
Relative When Ac = 38
Solution:

## Slide 13
200 | MOV AX | Mode
201 | Address = 500 | 
202 | Next Address | 
400 | 700 | 
500 | 800 | 
600 | 900 | 
702 | 325 | 
800 | 300 | 
Address Mode | Accumulator | Effective Address
Immediate | 500 | 201
Direct | 800 | 500
Indirect | 300 | 800
Relative | 325 | 702
Indexed | 900 | 600
Register indexed | 700 | 400
Ex 2: A two word instruction MOV AX, 500 stored at address 200 and 201. A processor register R1 contain 400 and the content of the index register XR is 100. Evaluate the effective address and the accumulator if the addressing mode is immediate, direct, indirect, relative, indexed and register indexed.
R1=400, XR= 100
(Hint: All Values in Hexadecimal)
Solution:

## Slide 14
Thank You For All
Adil-2018