## Slide 1
College : Mansour University
Department : Computer Science and information System
Prepared by
Dr. Adil Abbas Majeed
2018-2019
Architecture
Control Unit Design
Chapter Three

## Slide 2
Control Unit
Design of a Simple Computer
Computer Instruction
Instruction Cycles
Control of Common Bus
MicroProgrammed Control Unit
Program Control Instructions
Program Interrupt instruction
Outline

## Slide 3
1. Control Unit
External Input |  | Control Unit Subsystem |  | Command signal Status signal |  | Data processor subsystem |  | Output Data
 |  |  |  | Input Data |  |  |  | 
The design of a digital system can be divided into two distinct parts:
One part concerned with the design of the digital circuits that perform the data processing operations.
Second part is concerned with the design of the control circuits that supervise the operations and determine the sequence of microoperation required to execute the operation.
There are two types of control organization:-
Hardwired Control: The control logic is implemented with gates, flip-flops, decoders, and other digital circuits. It has the advantage that it can be optimized to produce a fast mode of operation.
Microprogrammed Control: It is a second alternative for designing the control unit of a digital computer. A computer that employs a microprogrammed control unit will have two separate memories: a main memory and a control memory.

## Slide 4
The minimum required to design a simple computer are:-
Memory (Address and Data buses): 4K  16
Registers: Six types of register
Address register AR
Program Counter PC
Data Register DR
Accumulator Processor register AC
Instruction Register IR
Temporary Register TR
Arithmetic Logic Shift Unit (ALSU).
Control Unit.
Common Bus System: It was used to ensure the connections between the simple computer memory and registers. It was constructed with 16 MUX of size 8  1 of three selection variable (C2 C1 C0) to determine the output to the bus.
2. Design of a Simple Computer

## Slide 5
C2 C1 C0 | Bus
0 0 0 | No thing
0 0 1 | AR
0 1 0 | PC
0 1 1 | DR
1 0 0 | AC
1 0 1 | IR
1 1 0 | TR
1 1 1 | Memory
Table: Bus Control
4096  16
Memory
Control
Unit
C2
Buses C1
C0
AR
PC
DR
AC
IR
TR
S3 S2 S1 S0
ALSU
Control Signal
Write Read
Address
7
1
2
3
4
5
6
16-Bits Common Bus System
Figure: Simple Computer Configuration.
H.W.: Design and draw a simple computer consist of
Memory 8k  32.
Registers (AR, PC, DR, AC, IR, TR, R1, R2 and R3).
Control unit (4 signals).
ALSU.
Number of instructions (60).

## Slide 6
3. Computer Instruction
15 12 | 11 0
Opcode | Address
Instruction | Hex. Code | Description
INC | 0 000 H | Increment AC
CMA | 1 000 H | Complement AC
SHR | 2 000 H | Shift Right AC
SHL | 3 000 H | Shift Left AC
LDA ADR | 4 H | Load Memory word to AC
STA ADR | 5 H | Store content of AC in memory
ADD ADR | 6 H | Add memory word to AC
AND ADR | 7 H | And memory word to AC
OR ADR | 8 H | Or memory word to AC
BUN ADR | 9 H | Branch Unconditionally
Instruction word of the simple computer consists of 16-bits.
Memory address = 4K i.e. 212 12-bits are needed to specify memory address.
The 4-bits opcode field means only 16 instruction 24 can be specified.
Table: Simple Computer Instruction Format
Table: Simple Computer Instruction
15 12 | 11 0
Opcode | Address

## Slide 7
4. Instruction Cycles
A program residing in the memory unit of the computer consists of a sequence of instructions. The program is executed in the computer by going through a cycle for each instruction. Each instruction cycle in turn is subdivided into a sequence of sub-cycles or phases. In the basic computer each instruction cycle consists of the following phases:
1. Fetch an instruction from memory.
2. Decode the instruction.
3. Execute the instruction.
Fetch Phase: Initially or First phase, the program counter PC is loaded with the address of the first instruction in the program. The sequence counter (SC) is cleared to 0, providing a decoded timing signal T0.
Decode Phase: Middle Phase, after fetching the instruction, it must be decoded to determine its type, this is performed in the next timing signal T2
T2: D0, • • •, D7  Decode IR(12-14), AR  IR(0-11)
Executing Phase: This is the last phase during it the instruction is executed and perform its required operation. It start with the timing signal T3 & when finished clear the sequence counter (SC  0) to return to the fetch phase.

## Slide 8
SC  0
AR  PC
IR  M[AR], PC  PC + 1
D0…D15  IR(12-15), AR  IR(0-11)
Execute the instruction M[AR], PC  PC + 1
Figure: Simple cycle flowchart
in a simple computer.
Operation | Description
Fetch | T0: AR  PC T1: IR  M[AR], PC  PC + 1
Decode | T2: D0 … D15  IR(12-15), AR  IR(0 + 11)
Execute | 
INC | D0T3: AC  AC + 1, SC  0
CMA | D1T3: AC  , SC  0
SHR | D2T3: AC  SHR(AC), SC  0
SHL | D3T3: AC  SHL(AC), SC  0
LDA ADR | D4T3: DR  M[AR] D4T4: AC  DR, SC  0
STA ADR | D5T3: M[AR]  AC, SC  0
ADD ADR | D6T3: DR  M[AR] D6T4: AC  AC + DR, SC  0
AND ADR | D7T3: DR  M[AR] D7T4: AC  AC  DR, SC  0
OR ADR | D8T3: DR  M[AR] D8T4: AC  AC  DR, SC  0
BUN ADR | D9T3: PC  AR, SC  0
Operation | Description
Fetch | T0: AR  PC T1: IR  M[AR], PC  PC + 1
Decode | T2: D0 … D15  IR(12-15), AR  IR(0 + 11)
Execute | 
INC | D0T3: AC  AC + 1, SC  0
CMA | 
SHR | D2T3: AC  SHR(AC), SC  0
SHL | D3T3: AC  SHL(AC), SC  0
LDA ADR | D4T3: DR  M[AR] D4T4: AC  DR, SC  0
STA ADR | D5T3: M[AR]  AC, SC  0
ADD ADR | D6T3: DR  M[AR] D6T4: AC  AC + DR, SC  0
AND ADR | D7T3: DR  M[AR] D7T4: AC  AC  DR, SC  0
OR ADR | D8T3: DR  M[AR] D8T4: AC  AC  DR, SC  0
BUN ADR | D9T3: PC  AR, SC  0
Table: Simple computer control function and microoperation.

## Slide 9
PC | Content of memory
128 | 7F40
512 | 1020
1000 | 3044
1500 | 7128
Example 1: What are the instructions that will be fetched and executed in the simple computer, then find value of AC, PC, AR, DR and IR after execute instructions?
Init: PC = 1500 , AC=4020
Solution
T0: AR←PC , AR ← 1500
T1: IR←M[AR], PC=PC +1, IR← M[1500] IR = 7128
T2: D0-D15←IR(12-15), AR←IR(0-11), AR=128
Fetch instruction D7 → AND ADDRES, AC = AC ^ DR
D7T3: DR←M[AR] , DR = M[128] , DR = 7F40
D7T4 : AC← AC ^ DR, AC ← 4020 ^ 7F40 , SC=0
End Values of registers
PC = 1501, AR = 128, DR = 7F40, IR = 7128, AC = 4020 ^ 7F40 = 4020

## Slide 10
5. Control of Common Bus
C2 C1 C0 | Bus
0 0 0 | No thing
0 0 1 | AR
0 1 0 | PC
0 1 1 | DR
1 0 0 | AC
1 0 1 | IR
1 1 0 | TR
1 1 1 | Memory
The 16-bit common bus is controlled by the selection inputs C2, C1, and C0. To derive the logic gates required to transfer a specific register to the bus, we scan all register transfer statements of table below:-
C2 C1 C0
T0: AR  PC 0 1 0
T1: IR  M[AR] 1 1 1
T2: AR  IR(0-11) 1 0 1
D4T3: DR  M[AR] 1 1 1
D5T3: M[AR]  AC 1 0 0
D6T3: DR  M[AR] 1 1 1
D7T3: DR  M[AR] 1 1 1
D8T3: DR  M[AR] 1 1 1
D9T3: DR  M[AR] 0 0 1
Table: Bus Control
Sol:
C0 = T1 + T2 + (D4 + D6 + D7 + D8 + D9)T3
C1 = T0 + T1 + (D4 + D6 + D7 + D8)T3
C2 = T1 + T2 + (D4 + D5 + D6 + D7 + D8)T3
D4
D6 T3
D7
D8 T2 C0
D9 T1
D4
D6 T3
D7
D8 T0 C1
T1
D4
D5 T3
D6
D7 T1 C2
D8 T2

## Slide 11
Instruction Format |  |  | 
31 29 | 28 23 | 22 5 | 4 0
Mode | Opcode | Memory address | Register address
31 29 | 28 23 | 5 | 4 0
Mode | Opcode (6-bits) | Memory address | Register address
10 9 | 8 3 | 2 0
00 | Opcode (6-bits) | 000
Example: A two-word instruction (ADD R, M) stored in memory of size 256 K × 16. If the instruction format of that computer has four fields: a memory address field, register field to specify one of 20 different register, a mode field to specify one of seven different modes and an opcode field.
Draw the instruction format of that computer and specify the maximum number of instructions computer that accommodate.
If the control memory of that computer is of size 2KB and each routine in this memory of eight microinstructions, perform the mapping process
Solution
16 × 2 = 32 bit total instruction
2N = 20 24 =16 or 25 = 32  N = 5 bits of register field
2M = 256K  M = 28 × 210 = 218 M=18 bits of memory address field
2K = 7 ; 22 = 4 or 23 = 8  K= 3 bits of mode field
Bits of opcode field=32-(5+18+3) = 6 bits; 26 = 64 Max no. of instructions
2K = 21 × 210 = 211 = 11bits of CM
2N = 8 N = 3 bits of routine field

## Slide 12
6. Microprogrammed Control Unit
It is a second alternative for designing the control unit of a digital computer. A computer that employs a microprogrammed control unit will have two separate memories: a main memory and a control memory.
The main memory is available to the user for storing the programs. The user's program in main memory consists of machine instructions and data.
The microprogram consists of microinstructions that specify various internal control signals for execution of register microoperations. Each machine instruction initiates a series of microinstructions in control memory. These microinstructions generate the microoperations to fetch the instruction from main memory; to evaluate the effective address, to execute the operation specified by the instruction, and to return control to the fetch phase in order to repeat the cycle for the next instruction.
Next address
generator
(Sequencer)
Control Address
Register (CAR)
Control Memory
(RAM)
Control Data Register (CDR)
External
Input
Control
Word
Figure: Microprogrammed control unit block diagram.
Next Address Information

## Slide 13
7. Program Control Instructions
A program control type of the instruction when executed may change the address value in the program counter (PC) and causes the flow of content to be altered.
Most of the program control instruction may be conditional or unconditional and this depends on the value of the status bits.
Status Bit Conditions
Skip Instruction
Branch and Jump instruction
Compare and Test Instructions
Subroutine Call and Return
Opcode | Subroutine first address
Subroutine Call and Return
A subroutine is a self-contained sequence of instructions that performs a given computational task. During the execution of a program, a subroutine may be called to perform its function many times at various points in the main program. A call subroutine instruction format is
The instruction is executed by performing:-
The address of the next instruction is pushed to the stack memory.
Control is transferred to the beginning of the subroutine.

## Slide 14
 |  |  |  |  |  | Main Memory | 
 |  |  |  |  | Execute | Call | Address
 |  | Stack Memory |  |  |  |  | 
SP-1 |  |  |  | PC |  | Next instruction | 
SP |  |  |  |  |  |  | 
Therefore the sequence of microoperation required to execute the call instruction are:
Call
The instruction that returns from the last subroutine is implemented by the microoperations. The sequence of microoperation for the return instruction are:
RET

## Slide 15
7. Program Interrupt Instruction
Program interrupt refers to the transfer of program control from a currently running program to another service program (Interrupt Service Routine ISR) as a result of an external or internal generated request. Control returns to the original program after the service program is executed.
The interrupt procedure is similar to a subroutine call except for three variations:
The interrupt is usually initiated by an internal or external signal rather than from the execution of an instruction.
The address of the interrupt service program is determined by the hardware rather than from the address field of an instruction.
An interrupt procedure usually stores all the information.
The state of the CPU at the end of the execute cycle is determined from:
1. The content of the program counter
2. The content of all processor registers
3. The content of certain status conditions
The collection of all status bit conditions in the CPU is sometimes called program status word a program status word or PSW. The PSW is stored in a separate hardware register and contains the status information that characterizes the state of the CPU.

## Slide 16
Types of interrupts
There are three major types of interrupts that cause a break in the normal execution of a program. They can be classified as:
External interrupts: External interrupts come from input-output (l/0) devices, from a timing device, from a circuit monitoring the power supply, or from any other external source.
Internal interrupts (TRAP): Internal interrupts arise from illegal or erroneous use of an instruction or data. Internal interrupts are also called traps. Examples of interrupts caused by internal error conditions are register overflow, attempt to divide by zero, an invalid operation code, stack overflow, and protection violation.
Software interrupts: which is initiated by executing instruction.

## Slide 17
Branch | Call | Interrupt
Initiated by the execution of an instruction. | Initiated by the execution of an instruction. | Initiated by an internal or external signal.
The branch address is given in the address field of the instruction | The address of subroutine is given in the address field of the call instruction | The address of the ISR is determined by the hardware
Does not store any information before branching | Store the value of the PC only before branching to the subroutine | Store all the information that define the state of the CPU
Conditional or Unconditional | Conditional or Unconditional | Unconditional
    What is the basic difference between a branch instruction, a call instruction and a program interrupts?
Internal | External
Initiated due to an error in the program itself | Initiated by an I/O device
Synchronous with the program | Asynchronous with the program
    What are the differences between internal and external interrupts?

## Slide 18
Thank You For All
Adil-2018