## Slide 1
College : Mansour University
Department : Computer Science and information System
Prepared by
Dr. Adil Abbas Majeed
2018-2019
Digital Image Processing
Introduction To DIP
Chapter One

## Slide 2
Computer Imaging
Computer Vision Application
Computer Imaging Systems
Digital Image Representation
Digitization
Image Sampling and Quantization
Types of Digital Images
Application of Image Processing
Computer Graphics
Image File Format
Outline

## Slide 3
1. Computer Imaging
Computer imaging can be separate into two primary categories:
1. Computer Vision.
2. Image Processing.
(In computer vision application the processed images output for use by a computer, whereas in image processing applications the output images are for human consumption).
Computer Vision is consists of
1. Image Analysis: involves the examination of the image data to facilitate solving vision problem. The image analysis process involves two other topics:
•Feature Extraction: It is the process of acquiring higher level image information, such as shape or color information.
•Pattern Classification: It is the act of taking this higher – level information and identifying objects within the image.

## Slide 4
2. Computer Vision Application
Computer vision systems are used in many and various types of environments, such as:
Manufacturing Systems: computer vision is often used for quality control, where the computer vision system will scan manufactured items for defects, and provide control signals to a robotics manipulator to remove detective part automatically.
Medical Community: Current example of medical systems to aid neurosurgeons (جراحة الاعصاب) during brain surgery, systems to diagnose skin tumors (سرطان الجلد) automatically.
Law Enforcement: The field of Law Enforcement and security in an active area for computer vision system development, with application ranging from automatic identification of fingerprints to DNA analysis.
Infrared Imaging (صور تحت الحمراء).
Satellites Orbiting (مدار الفضائيات).

## Slide 5
3. Computer Imaging Systems
Computer Imaging Systems (Components of an image processing system)
They are comprised of two primary components types, hardware and software. The hard ware components can be divided into image acquiring sub system (computer, scanner, and camera) and display devices (monitor, printer).The software allows us to manipulate the image and perform any desired processing on the image data.

## Slide 6
An image may be defined as a two-dimensional function f(x, y), where x and y are spatial (plane) coordinates, and the amplitude of f at any pair of coordinates (x, y) is called the intensity or gray level of the image at that point. When x, y, and the amplitude values of f are all finite, discrete quantities, we call the image a digital image.
4. Digital Image Representation

## Slide 7
An image may be continuous with respect to the X and Y coordinates and also in amplitude so that it can be suitable for computer processing.
Digitization: It is process of transforming standard video signal into a digital image. Its mean using discrete values instead of continuous values. The analog video signal is turned into a digital image by sampling the continuous signal at affixed rate.
5. Digitization

## Slide 8
6. Image Sampling and Quantization
The output of most sensors is a continuous voltage waveform whose amplitude and spatial behavior are related to the physical phenomenon being sensed. To create a digital image, we need to convert the continuous sensed data into digital form. This involves two processes: sampling and quantization.
Sampling: It is the digitization of gray levels so that only discrete values of gray levels are used.
Quantization: It is digitization of spatial coordinates (x, y) so that there are gray level for discrete values of x and y.

## Slide 9
Example 1: What is the amount of storage required in (bits, bytes) to store image with Width = 200 pixels and height = 100 pixels given that the number of gray scale levels used to represent the image is (256 or 16) levels?
Solution:
28 = 256  bits = 8
24 =16  bits = 4
In bits
The total size of image in (bits)= widthheight  bits = 2001008 = 160000 bits
The total size of image in (bits)= widthheight  bits = 200  1004 = 80000 bits
In bytes
The total size of image in (bytes)=widthheightbytes =2001001=10000 bytes
The total size of image in (bytes) =widthheightbytes=200100 =5000 bytes
Example 2: If we have (6 bit) in 128  128 image .Find the no. of gray levels to represent it, then find the no. of bit in this image?
Solution:
No. of gray Level = 26 = 64 Gray Level
The total size of image in (bits) = width  height  bits
No. of bits = 128  128  6 = 9.8304  104 bits.

## Slide 10
7. Types of Digital Images
There are consisting of four types below:
Binary image.
Gray scale image
Color image
Multispectral image
Binary image: A binary image is a digital image that has only two possible values for each pixel. Typically the two colors used for a binary image are black and white though any two colors can be used. The color used for the object(s) in the image is the foreground color while the rest of the image is the background color. Binary images are also called bi-level or two-level. This means that each pixel is stored as a single bit—i.e., a 0 or 1.
Ex.: segmentation, thresholding, OCR (Optical Character Recognition)
Gray scale image: Gray scale is a range of shades of gray without apparent color. The darkest possible shade is black, which is the total absence of transmitted or reflected light. The lightest possible shade is white. It is referred to as monochrome, or one color image. They contain brightness information only, no color information. The number of bits used for each pixel determines number of different brightness level available. The typical image contains 8bits/pixel data, which allows us to have 256 (0-255) different brightness (gray) levels. Ex.: luminance, Signal to noise

## Slide 11
Color image: A (digital) color image is a digital image that includes color information for each pixel. A color image has three values per pixel and they measure the intensity and chrominance of light. Typically color image are represented as red, green, blue, or RGB images. Using 8-bits monochrome standard as a model, corresponding color images have 24 bits /pixel (8-bits for each of the three color bands (red, green, blue)). The RGB color space is commonly used in computer displays. A color image is usually stored in memory as a raster map.
Ex.: Color photography, TV, and Camera
Multispectral Images: It is one that captures image data at specific frequencies across the electromagnetic spectrum. Multispectral images typically contain information outside the normal human perceptual range. This may include infrared (تحت الحمراء), ultraviolet (فوق البنفسجيه), X-ray, acoustic (سمعي) or radar data. Source of these types of image include satellite systems, underwater sonar systems and medical diagnostics imaging systems.
Ex.: infrared, ultraviolet, x-ray, acoustic, or radar.

## Slide 12
8. Application of Image Processing
Automatic Visual Inspection System
Remotely Sensed Scene Interpretation
Biomedical Imaging Techniques
Defense surveillance
Content-Based Image Retrieval
Moving- object Tracking
Image and Video Compression

## Slide 13
9. Computer Graphics
Computer graphics is a specialized field within that refers to the computer science realm that refers to the reproduction of visual data through the use of computer.
In computer graphics, types of image data are divided into two primarily categories:
1. Bitmap image (or raster image): can represented by our image model I(r, c), where we have pixel data and corresponding brightness values stored in file format.
2. Vector images: refer to the methods of representing lines, curves shapes by storing only the key points. These key points are sufficient to define the shapes, and the process of Turing theses into an image is called rending after the image has been rendered, it can be thought of as being in bit map format where each pixel has specific values associated with it.

## Slide 14
10. Image File Format
We will present some of the most popularly used Image file format standards.
BMP format: It is the format used by the windows, it’s a compressed format and the data of image are located in the field of data while there are two fields, one for header (54 byte) that contains the image information such as (height ,width , no. of bits per pixel, no. of bands, the file type).
Tagged Image Format (.tif, .tiff): The .tif format is a very broad format, which can handle anything from bitmaps to compressed color palette images. This format is popular, relatively simple, and allows color.
Portable Network Graphics (.png): This is an extensible file format that provides lossless, well compressed storage of raster images.
JPEG (.jpg): It is the most widely used standard for transmission of pictorial information and includes a variable lossy encoding as part of the standard, set by a quality parameter.
MPEG (.mpg): This format is extensively used throughout the Web and is used only for motion images. This uses compression, yielding only lossy videos.
Graphics Interchange Format (.gif): This format supports 8-bit color palette images and is not very popular among the image processing researchers.
VIP (visualization in image processing) formats: It is developed for the CVIP (Computer vision image Processing) tools software. To represent this type of data the remapping is used, which is the process of taking original image and adding an equation to translate it to the range (0-225).

## Slide 15
Thank You For All
Adil-2018